## Slide 1: CS4100: Computer Architecture Instructions: Language of the Computer (I)
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Adapted from textbook slides https://www.elsevier.com/books-and-journals/book-companion/9780128122754/lecture-slides)

## Slide 2: Introduction
To command a computer, you must speak its language
Most computers understand high-level languages (HLL), e.g., C, C++, Java, with suitable compilers
How about language to a computer’s hardware?
  Assembly language  machine instructions
  Very close to control signals to control hardware operations
foo(int v[], int k) {
int temp;
temp = v[k];
v[k] = v[k]+v[k+1];
v[k+1] = temp;
}
Variables (memory locations storing date)
Operators
operations on operands
operands of operators

## Slide 3: Outline
Languages of computers (Sec. 2.1)
Operations of computer hardware (Sec. 2.2)
Operands of computer hardware (Sec. 2.3, 2.4)
  Registers, memory, signed and unsigned numbers
Representing instructions (Sec. 2.5)
More operations: logic, decision making (Sec. 2.6, 2.7)
Supporting procedures in hardware (Sec. 2.8)
More operand representations (Sec. 2.9, 2.10)
  Characters, wide immediates and addresses
Parallelism and instructions (Sec. 2.11)
Translating and starting a program (Sec. 2.12)

## Slide 4: Outline
A C sort example to put it all together (Sec. 2.13)
Arrays versus pointers (Sec. 2.14)
Compiling C and interpreting Java (Sec. 2.15)
Other ISAs: MIPS, x86 (Sec. 2.16, 2.17)
The rest of RISC-V (Sec. 2.18)
Fallacies and pitfalls (Sec. 2.19)

## Slide 5: Outline
Languages of computers (Sec. 2.1)
Operations of computer hardware (Sec. 2.2)
Operands of computer hardware (Sec. 2.3, 2.4)
  Registers, memory, signed and unsigned numbers
Representing instructions (Sec. 2.5)
More operations: logic, decision making (Sec. 2.6, 2.7)
Supporting procedures in hardware (Sec. 2.8)
More operand representations (Sec. 2.9, 2.10)
  Characters, wide immediates and addresses
Parallelism and instructions (Sec. 2.11)
Translating and starting a program (Sec. 2.12)

## Slide 6: Language to Computer Hardware
Z
N
Register
Memory
01001101
Controller
ALU
clock
Control signals
Datapath
Control
PC
IR
10110100
10110100
Instruction: words of a computer’s language
Instruction set: vocabulary of the language
add r1,r2,r3
01001101
0011
0100
0111
+
Notes: 0s and 1s in the instructions become signals to control the datapath

## Slide 7: Language to Computer Hardware
Different computers have different languages (instruction sets)
  But with many aspects in common
  Because all computers are constructed from hardware technologies based on similar underlying principles
  Because there are a few basic operations that all computers must provide
    Makes it easy to build the hardware and the compiler while maximizing performance and minimizing cost and energy
    Combinations of these basic operations allow a computer to run all sorts of programs written in various HLLs
What are the most basic operations and how to specify them?
Notes: What must a food processor have in order to make all kinds of cooking?

## Slide 8: Essentially, We Are Asking …
What must be specified in an instruction set architecture (ISA)?
  “ISA encompasses all the information necessary to write a machine language program that will run correctly”
  Including:
  operations: +, -, *, /, ...
  operands (data, address)
  flow control
Processor
Operating System
Application
Digital Design
Circuit Design
Transistors
HW
SW
Compiler
Assembler
Memory
I/O System
ISA
Datapath & Control
What are included in ISA and how are they specified have profound effects on computer design!

## Slide 9: Components of an ISA
Storage and data: (operands)
Organization of programmable storage:
  Registers: # of bits, # of registers, their roles, …
  Memory: addressing, access methods, …
Data types and data structures
  Integers, floating-point, text, signed number, …
Operations on data and execution flow control:
Instruction set (or operation code)
  ALU, control transfer, exceptional handling
Instruction specification:
Instruction format and encoding

## Slide 10: Use 64-bit RISC-V (RV64) as an Example
Developed at UC Berkeley as open ISA
  Now managed by the RISC-V Foundation (riscv.org)
Typical of many modern ISAs
Similar ISAs have a large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
We will not only describe what the RISC-V ISA is
But also study the principles behind the design
And examine some different design options to appreciate why RISC-V chooses the specific option

## Slide 11: Outline
Languages of computers (Sec. 2.1)
Operations of computer hardware (Sec. 2.2)
Operands of computer hardware (Sec. 2.3, 2.4)
  Registers, memory, signed and unsigned numbers
Representing instructions (Sec. 2.5)
More operations: logic, decision making (Sec. 2.6, 2.7)
Supporting procedures in hardware (Sec. 2.8)
More operand representations (Sec. 2.9, 2.10)
  Characters, wide immediates and addresses
Parallelism and instructions (Sec. 2.11)
Translating and starting a program (Sec. 2.12)

## Slide 12: What Basic Operations for Hardware?
Operations to work on data
  Arithmetic (+, -, *, /), logic (&, |, ~)  similar to a function, e.g. z=f(x,y), operating on values
  2-operand (a + b), 1-operand (++a)
Operations to move and copy data between storage locations
  As storage, original location still retains the data, until explicitly overwritten
Operations to change execution flow
  Unconditional: goto, jump to new location to execute
  Conditional: if-then-else, jump if condition is true
  Procedural: foo(), similar to goto but need to come back

## Slide 13: Let’s Start with Arithmetic Operations
The most basic operation for any computer hardware is arithmetic operation on numbers, e.g., a = b + c
Basic RISC-V arithmetic instructions are specified as:
  add a,b,c # a  b + c
All RISC-V arithmetic instructions have this form
  3-address: a, b, c are storage locations that hold data, but c may also be a value
Design Principle 1: Simplicity favors regularity
Regularity makes implementation simpler
Simplicity enables higher performance at lower cost
vs. Flexibility
Why storage concept indispensable?

## Slide 14: Arithmetic Instruction Example
C code:
f = (g + h) - (i + j);
Compiled RISC-V (pseudo) code:
add t0, g, h # temp t0  g + h add t1, i, j # temp t1  i + j sub f, t0, t1 # f  t0 - t1
  t0 and t1 are temporary variables, i.e., storage locations, normally allocated by the compiler

## Slide 15: Why 3-Address Format: add a,b,c?
Why not 2-address format? add b,c # b  b + c
  Still regular, and one address less to specify and encode!
How about 0-address format? add
  Where to get the operands?
   must be specified implicitly so that the computer hardware knows where to get, e.g. in a stack add #stack[top]stack[top]+stack[next]
Tradeoff between flexibility and complexity

## Slide 16: Outline
Languages of computers (Sec. 2.1)
Operations of computer hardware (Sec. 2.2)
Operands of computer hardware (Sec. 2.3, 2.4)
  Registers, memory, signed and unsigned numbers
Representing instructions (Sec. 2.5)
More operations: logic, decision making (Sec. 2.6, 2.7)
Supporting procedures in hardware (Sec. 2.8)
More operand representations (Sec. 2.9, 2.10)
  Characters, wide immediates and addresses
Parallelism and instructions (Sec. 2.11)
Translating and starting a program (Sec. 2.12)

## Slide 17: Operands to an Operation
Operands may be the value itself (immdiates) add a,b,3 or the storage location holding the value add a,b,c
The storages that can hold values may be in memory or in registers
  Registers are a small number of storage locations built directly into CPU hardware; memory refers to storage locations in the main memory  need to specify addresses
  How about disk? Why not disk locations as operands?
RISC-V arithmetic instructions must use register operands!
2
1
3

## Slide 18: Why Restricted to Register Operands?
Why not allow memory operands, too? add M[1000],M[2019],M[2020]
  Registers are inside CPU  same clock as CPU, connect directly to arithmetic units, short and fast signals
  Registers are small  easy to activate to access data, short and fast signals
  Registers are small  fewer number of bits to specify and encode  smaller instructions
  Suitable for holding frequently accessed data
Design Principle 2: Smaller is faster
Register vs. main memory (millions of locations)

## Slide 19: How to Specify (1) Register Operands?
Must know RISC-V register organization!
RISC-V has a 32 × 64-bit register file
  32 registers specified as x0 to x30, each with a 5-bit addr
x0 constant 0 | x10 x11
x1 return address | 
x2 stack pointer | 
x3 global pointer | 
x4 thread pointer | x18 saved registers x27
x8 frame pointer | 
x9 saved registers | 
x28
x31


x12
x17

x5
x7

temporaries
temporaries
function arguments/results
function arguments
Why not 64, or 16?
doubleword
Notes: Why not 64? Small is fast! Number of bits for encoding an instruction.

## Slide 20: Register Operand Example
How to do the following C statement?
  f = (g + h) - (i + j);
  Assume that f, g, h, i, j are in x19, x20, x21, x22, x23
Use intermediate temporary registers x5, x6
  add x5,x20,x21 # x5  g + h
  add x6,x22,x23 # x6  i + j
  sub x19,x5,x6 # f  x5 – x6
  If data are in the memory, they must be loaded into the registers first before arithmetic operations can be operated on them; after operations, they need to be stored back
Use data transfer instructions (ld, sd, ...) discussed later
Notes: Why not get rid of memory altogether?

## Slide 21: How to Specify (2) Memory Operands?
Must know RISC-V memory organization!
  Main memory is organized as a 1D array of locations
  Each location can hold one byte of data and is identified by an address  memory is byte addressed, i.e. each address identifies an 8-bit byte of data, ranging from 0 to 261
A nature way of specifying memory operands in RISC-V is like addressing an array, e.g., A[100]
  A is the base address and 100 is the offset and memory address of A[100] is (A + 100)
  In RISC-V, memory operand is specified as: 100(x22), where x22 contains base addr. and 100 is offset (in bytes)
  A memory operand normally gets a doubleword (64 bits), and thus word addresses differ by 8
Notes: Why not word-addressed?

## Slide 22: Memory Operand Example
C code:
A[9] = h + A[8];
  h in x21, base address of A in x22
  A[8]: the 8th doubleword in array A[], which is at the 64th byte from start of A[]
Compiled RISC-V code:
ld x9, 64(x22) add x9, x21, x9 sd x9, 72(x22)
offset
base register
…
…
…
264 - 1
0
A = 1024
A[8] = 1088
A[9] = 1096
load doubleword
store doubleword

## Slide 23: Registers and Memory Size
64 bit address | data
0x 0000 0000 0000 0000 | 
0x 0000 0000 0000 0001 | 
0x 0000 0000 0000 0002 | 
0x 0000 0000 0000 0003 | 
0x 0000 0000 0000 0004 | 
0x 0000 0000 0000 0005 | 
0x 0000 0000 0000 0006 | 
0x 0000 0000 0000 0007 | 
… | 
0x FFFF FFFF FFFF FFFF | 
Memory
RISC-V I64 CPU
x0 | 0
x1 | 
x2 | 
… | 
x31 | 
double word
=64 bits
1byte=8bits
double word=64 bits
5 bits for register ID
Note: actual physical address bits are less than 64, e.g., 42 for Intel x86_64
(Prof. Jing-Jia Liou)

## Slide 24: More about RISC-V Memory Organization
RISC-V is Little Endian
  Least-significant byte at least address of a word
  c.f. Big Endian: most-significant byte at least address
(By R. S. Shaw - Own work, Public Domain, https://commons.wikimedia.org/w/index.php?curid=2974661)

## Slide 25: More about RISC-V Memory Organization
RISC-V does not require words to be aligned in memory, i.e., at an address a multiple of 4 (for a word) or 8 (for a doubleword)
    Unlike some other ISAs; but misaligned memory accesses may be very very slow
0 1 2 3
Aligned
Not
Aligned
…
…
…
264 - 1
0
A = 1024
A[8] = 1088
A[9] = 1096
Aligned
Not
Aligned
Notes: Why need to aligned?

## Slide 26: Registers vs. Memory
Registers are faster to access than memory
  But, operating on memory data requires loads and stores
    More instructions to be executed, larger code size
Compilers should use registers for variables as much as possible
  Only spill to memory for less frequently used variables, if more variables than available registers are used
  Register optimization is important!
Why not keep all variables in memory?
  Smaller is faster: registers are faster than memory
  Registers are more versatile:
    Register file can read 2 and write 1 registers per instruction
    Memory read/write 1 operand per instruction, no operation

## Slide 27: How about (3) Immediate Operands?
Small constants used frequently (50% of operands) e.g., A = B + 4; if (C > 1) … ;
Put 'typical constants' in memory and load them
  ld x9, AddrConstant4(x3)
  add x22, x22, x9
Alternative: constant data specified in the instruction addi x22, x22, 8
Immediate operand
Design Principle 3: Make the common case fast
Small constants are common
Immediate operand avoids a load instruction
Too slow
Why define a new instruction, addi? Why not reuse add?

## Slide 28: Handling Constant Zero and Negatives
The number zero (0) is so common in code that RISC-V hardwired register 0 (x0) to 0
  Cannot be overwritten, e.g., addi x0,x0,5 (no effect)
  Useful for other common operations, too, e.g., move between registers: add x22, x20, x0
    Thus, there is no need to implement a move instruction in hardware  simpler CPU design and implementation
No need for subtract immediate instruction either
  Just use a negative constant: addi x22, x22, -8
Time to review signed and unsigned numbers

## Slide 29: Represent Unsigned Binary Integers
Given an n-bit number
Use all the bits to represent values
Example: (32 bits)
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Range: 0 to +2n – 1
  Using 32 bits: 0 to +4,294,967,295
  Using 64 bits: 0 to +18,446,774,073,709,551,615
…
Can get the max value

## Slide 30: Signed Binary Integers (2’s-Complement)
Given an n-bit number
Use bit 31/63 to represent sign (sign bit)
  1 for negative and 0 for non-negative numbers
Signed negation: complement (1 → 0, 0 → 1) & add 1
  Non-negative numbers have the same representation
  –(–2n – 1) can’t be represented
Example: (32 bits)
  1111 1111 1111 1111 1111 1111 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
…
Notes: The negation or complement of a number x is 2^n − x, or its “two’s complement.”

## Slide 31: 2’s-Complement Signed Integers
Range: –2n – 1 to +2n – 1 – 1
  Using 32 bits: –2,147,483,648 to +2,147,483,647
  Using 64 bits: −9,223,372,036,854,775,808 (1000 … 00002) to 9,223,372,036,854,775,807 (0111 1111 … 11112)
  0: 0000 0000 … 00002
  –1: 1111 1111 … 11112 (least negative number)
  Most-negative number (1000 … 00002) does not have a corresponding positive number
Why 2’s complement?
Signed/unsigned +/- treated the same!
One adder, no distinction
SW interprets meaning
Notes: Sign bits can be manipulated in the same way as value bits  unsigned and signed number additions can be done by the same adder hardware; there is no need to distinguish which is which

## Slide 32: Sign Extension
Representing a number using more bits while preserving the numeric value
How to do? replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010  0000 0000 0000 0010
  –2: 1111 1110  1111 1111 1111 1110
In RISC-V instruction set
  lb: load byte (sign-extend loaded byte)
  lbu: load byte unsigned (zero-extend loaded byte)
Sign?
lb x22,0(x21)
lbu x22,0(x21)
FFFFFF
000000
F7
F7
Notes: What matters is how software interprets the bits

## Slide 33: Outline
Languages of computers (Sec. 2.1)
Operations of computer hardware (Sec. 2.2)
Operands of computer hardware (Sec. 2.3, 2.4)
  Registers, memory, signed and unsigned numbers
Representing instructions (Sec. 2.5)
More operations: logic, decision making (Sec. 2.6, 2.7)
Supporting procedures in hardware (Sec. 2.8)
More operand representations (Sec. 2.9, 2.10)
  Characters, wide immediates and addresses
Parallelism and instructions (Sec. 2.11)
Translating and starting a program (Sec. 2.12)

## Slide 34: How to Specify RISC-V Instructions?
Now that we have learned operations and operands of computer hardware, let us study how to put them together to form computer instructions
  Remember: Computer only understands 1s and 0s, so “add x21,x22,x23” is meaningless to hardware
  Instructions to instruct computer hardware how to operate should also be encoded in binary, called machine code
RISC-V’s strategies for instruction encoding
  Encode every instruction in 32-bit words, divided into fields
  Small number of formats encoding operation code (opcode), register numbers, …
Let’s look at three of them first
Regularity!
Why not just 1 format?

## Slide 35: RISC-V R-format Instructions
For register to register operations
Instruction fields
  opcode: operation code
  rd: destination register number
  funct3: 3-bit function code (additional opcode)
  rs1: the first source register number
  rs2: the second source register number
  funct7: 7-bit function code (additional opcode)
Why not combine op and funct?
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
Notes: Question: Why aren’t opcode and funct a single 12-bit field?

## Slide 36: R-format Example
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
add x9,x20,x21
0000 0001 0101 1010 0000 0100 1011 0011two = 015A04B316
0
21
20
9
0
51
0000000
10101
10100
01001
000
0110011
0
x21
x20
x9
0
add

## Slide 37: RISC-V I-format Instructions
Immediate arithmetic and load instructions
  rs1: source or base address register number
  immediate: constant operand, or byte offset to base addr
    2’s-complement, sign extended, −211 to 211−1
Design Principle 3: Good design demands good compromises
Different formats complicate decoding, but allow 32-bit instructions uniformly
Keep formats as similar as possible (only 1 field differs)
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits
Notes: Particularly, op code is still at the same location and takes 6 bits

## Slide 38: I-Format Example 1
RISC-V instruction:
addi x9,x22,-50
  opcode = 19 (look up in RISC-V Manual)
  rs1 = 22 (source operand register number)
  rd = 9 (destination register number)
  immediate = -50 (by default, this is decimal)
Decimal representation:
Binary representation:
-51
22
9
0
19
1111 1100 1101
10110
01001
000
0010011

## Slide 39: I-Format Example 2
RISC-V instruction:
ld x9,120(x22)
  opcode = 3 (look up in RISC-V Manual)
  rs1 = 22 (base address register number)
  rd = 9 (destination register number)
  immediate = 120 (offset)
Decimal representation:
Binary representation:
120
22
9
3
3
0000 0111 1000
10110
01001
011
0000011

## Slide 40: RISC-V S-format Instructions
Different immediate format for store instructions
  rs1: base address register number
  rs2: source operand register number
  immediate: offset added to base address
    Split so that rs1 and rs2 fields always in the same place
RISC-V instruction:
sd x9,120(x22)
imm[11:5]
rs2
rs1
imm[4:0]
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
120-1
9
22
120-2
3
35
0000011
01001
10110
11000
011
0100011
Notes: 120 = 0000 0111 1000

## Slide 41: Key Computer Design Principles
Computer instructions represented as numbers
Program instructions can be stored at the same place as data (in memory) and be manipulated in the same way as data  stored-program computer
  Instructions and data look the same, just 0s and 1s
  Differ only in how you interpret the bits
One consequence: everything addressed
  Everything has a memory address: instructions, data
    Both branches and jumps use these
  One register keeps address of the instruction being executed: “Program Counter” (PC)
  Register can hold any 64-bit value, (signed) int, address, etc.

## Slide 42: Stored-Program Computers
Consequence #2: programs can operate on programs
  e.g., compilers, linkers, …
  The latter is data to the former
Consequence #3: binary compatibility
  Programs can be shipped as files of binary numbers and executed on any computers with a compatible ISA
Consequence #4: fast context switches of processes
Fig. 2.7
Notes: Memory can contain the source code for an editor program, the corresponding compiled machine code, the text that the compiled program is using, and even the compiler that generated the machine code.

## Slide 43: Stored Program with Memory Access
address | instruction/data
 | ld x20, 0(x10)
 | ld x21, 0(x11)
 | add x9, x20, x21
 | sd x9, 0(x12)
b | 10
c | 20
a | 30
 | …
Memory
Instruction Register
CPU
add x9, x20, x21
10
20
30
1
2
3
4
adder
(1) load b to x18=10
(2) load c to x19=20
(3) add x9=x18+x19
(4) store x9 to a
3
1
2
4
Assume
x10=b’s address
x11=c’s address
x12=a’s address
load
instr.
(Prof. Jing-Jia Liou)

## Slide 44: Instruction and Data Encoding (in Hex)
address | instruction/data
 | 00053A0316
 | 0005BA8316
 | 015A04B316
 | 0096302316
b | 0000000A16
c | 0000001416
a | 0000001E16
 | …
Memory
Instruction Register
CPU
015A04B316
0000000A16
0000001416
0000001E16
adder
Assume
x10=b’s address
x11=c’s address
x12=a’s address
(Prof. Jing-Jia Liou)

## Slide 45: Outline
Languages of computers (Sec. 2.1)
Operations of computer hardware (Sec. 2.2)
Operands of computer hardware (Sec. 2.3, 2.4)
  Registers, memory, signed and unsigned numbers
Representing instructions (Sec. 2.5)
More operations: logic, decision making (Sec. 2.6, 2.7)
Supporting procedures in hardware (Sec. 2.8)
More operand representations (Sec. 2.9, 2.10)
  Characters, wide immediates and addresses
Parallelism and instructions (Sec. 2.11)
Translating and starting a program (Sec. 2.12)

## Slide 46: Bitwise Operations
Up until now, we have seen arithmetic (add, addi) and memory access (ld, sd)
  All of these instructions view contents of register as a single quantity (such as a signed or unsigned integer)
New perspective: View contents of register as 64 individual bits rather than as a single 64-bit number
  Since registers are composed of 64 bits, we may want to access individual bits rather than the whole
Introduce two new classes of instructions:
  Logical operators
  Shift instructions

## Slide 47: Logical and Shift Operations
Instructions for bitwise manipulation
  Useful for extracting and inserting groups of bits in a word
Operation | C | Java | RISC-V
Shift left | << | << | sll, slli
Shift right | >> | >>> | srl, srli
Shift right arith. | >> | >> | sra, srai
Bitwise AND | & | & | and, andi
Bitwise OR | ¦ | ¦ | or, ori
Bitwise XOR | ^ | ^ | xor, xori
Bitwise NOT | ~ | ~ | 
Fig. 2.8
Notes: One way to implement NOT is to use XOR with one operand being all ones (0xFFFF FFFF FFFF FFFF).

## Slide 48: Shift Operations
sll: shift left logical (R-type)
  Shift left and fill with 0 bits
  Shift left by i bits = multiplies by 2i (faster than multiply)
Example: sll x9,x20,x21
  x20 = 0000 … 0001; x21 = 0000 … 0011 = 3
  After instruction executed, x9 will contain 0000 … 1000
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
0000000
10101
10100
01001
001
0110011
0
x21
x20
x9
1
sll

## Slide 49: Shift Operations
srl: shift right logical (R-type)
  Shift right and fill with 0 bits
  Shift right by i bits = divides by 2i (unsigned only) (much faster than division, used in compiler optimization)
  Example: srl x9,x20,x21
sra: shift right arithmetic (R-type)
  Shift right and fill with sign bits (no sla!)
  Shift right by i bits = divides by 2i (signed)
  Example: sra x9,x20,x21
    x20 = 1111 … 1000; x21 = 0000 … 0011 = 3
    After instruction executed, x9 will contain 1111 … 1111
0100000
10101
10100
01001
101
0110011
0000000
10101
10100
01001
101
0110011
Note the encoding

## Slide 50: Shift Immediate Operations
slli: shift left logical immediate (32-bit RISC-V: RV32)
  shamt: how many bits to shift
    32-bit data can only be shifted 32 bit positions  5-bit shamt
    Same format as R-type, except rs2 becomes shamt
slli: how about 64-bit RISC-V (RV64)?
  We can shift 64 bit positions and need 6 bits for shamt
  How?
rs1
rd
001
0010011
6 bits
7 bits
5 bits
5 bits
3 bits
000000
shamt
6 bits
0000000
shamt
rs1
rd
001
0010011
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits

## Slide 51: Logic Operations
and: useful for setting certain portions of a word to 0s, while leaving the rest alone  masking
  Example: and x9,x10,x11
or: useful for forcing certain bits of a word to 1s, while leaving others unchanged
  Example: or x9,x10,x11
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
00000000 00000000 00000000 00000000 00000000 00000000 00111100 00000000
00000000 00000000 00000000 00000000 00000000 00000000 00001100 00000000
x10
x11
x9
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
00000000 00000000 00000000 00000000 00000000 00000000 00111100 00000000
00000000 00000000 00000000 00000000 00000000 00000000 00111101 11000000
x10
x11
x9

## Slide 52: Logic Operations
xor: differencing operation
  Set some bits to 1, leave others unchanged
xor x9,x10,x12
  If mask (x12) = 1, 0  1 and 1  0
  If mask (x12) = 1, 0  0 and 1  1
  So, if mask is all 1s, XOR becomes a NOT operation  no need for a not instruction (2-address) in RISC-V
00000000 00010100 00000000 00000000 00000000 00000000 00001101 11000000
x10
x12
x9
11111111 11000011 11111111 11111111 11111111 11111111 11111111 11111111
11111111 11010111 11111111 11111111 11111111 11111111 11110010 00111111
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
XOR

## Slide 53: So Far...
All instructions studied so far have allowed us to manipulate data
So we have built a calculator
However, in order to build a computer, we need the ability to make decisions and change the execution flow

## Slide 54: Conditional Branch Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs1,rs2,L1
  if (rs1 == rs2) branch to instruction labeled L1, i.e., load memory address of that instruction to PC (Program Counter), so that the CPU will next fetch and execute the branch-to instruction
bne rs1,rs2,L1
  If (rs1 != rs2) branch to instruction labeled L1 by storing L1 (an address) into PC
Memory address

## Slide 55: Compiling If Statements
C code:
if (i==j) f = g + h; else f = g - h;
  f, g, h, i, j in x19, x20, x21, x22, x23
Compiled RISC-V code:
bne x22,x23,Else add x19,x20,x21 beq x0,x0,Exit // unconditional Else: sub x19,x20,x21 Exit: …
Assembler calculates address
(discussed later)
Exit:
i == j?
f=g+h
f=g-h
(false) i != j
(true) i == j
Else:
Why not unconditional jump?
Notes: Encoding will be discussed in later chapter

## Slide 56: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in x22, k in x24, base address of save[] in x25
Compiled RISC-V code:
Loop: slli x10,x22,3 // x10i*8 add x10,x10,x25 // x10save[i] ld x9,0(x10) bne x9,x24,Exit addi x22,x22,1 beq x0,x0,Loop Exit: …

## Slide 57: Concept of Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
A compiler identifies basic blocks for optimization
  All instructions in a basic block will surely be executed once the basic block is entered  can rearrange execution seq.
An advanced processor can accelerate execution of basic blocks

## Slide 58: More Conditional Branch Operations
blt rs1,rs2,L1
  if (rs1 < rs2) branch to instruction labeled L1
bge rs1,rs2,L1
  if (rs1 >= rs2) branch to instruction labeled L1
Example:
  if (a > b) a += 1;
  a in x22, b in x23
  bge x23,x22,Exit // branch if b >= a
  addi x22,x22,1
  Exit:

## Slide 59: Signed vs. Unsigned Comparison
Signed comparison: blt, bge
Unsigned comparison: bltu, bgeu
Example:
  x22 = 1111 1111 1111 1111 1111 1111 1111 1111
  x23 = 0000 0000 0000 0000 0000 0000 0000 0001
  blt x22,x23,L1 # signed
  –1 < +1  branch to L1
  bltu x22,x23,L1 # unsigned
  +4,294,967,295 > +1  do not branch

## Slide 60: Branch Instruction Design
Alternative 1: (MIPS approach)
  Set a register based on comparison result (e.g., slt), then branch on the value in that register with beq or bne
  Pro: hardware for <, ≥, … slower than =, ≠, because combining with branch involves more work per instruction, requiring a slower clock  all instructions penalized!
  Con: need two instructions instead of one
Alternative 2: (ARM approach)
  Keep extra bits (condition codes or flags) that record what occurred during an instruction, e.g., overflow, negative, …
  Conditional branches then test on condition codes
  Con: will create dependencies on condition codes