## Slide 1: CS4100: Computer Architecture The Processor (III)
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Outline
Problem statement and logic review (Sec. 4.1, 4.2)
Building a simple RISC-V processor with datapath and control (Sec. 4.3, 4.4)
Building a pipelined RISC-V processor with datapath and control (Sec. 4.5, 4.6)
Dealing hazards in pipelined processor: data and control hazards (Sec. 4.7, 4.8)
Handling exceptions (Sec. 4.9)
More advanced topics: parallelism via instructions, ARM Cortex-A53 and Intel Core i7 Pipelines, instruction-level parallelism (Sec. 4.10, 4.11, 4.12)

## Slide 3: Pipeline Hazards
Situations that prevent starting the next instruction in the next cycle, e.g.,
add x19,x0,x1 sub x2,x19,x3
Note: Data flow between instructions through registers
Time
add x19,x0,x1
sub x2,x19,x3
ALU
IM
Reg
DM
Reg
ALU
IM
DM
Reg
Reg
sub would read old data

## Slide 4: Three Types of Pipeline Hazards
Structure hazards
  Conflict for use of a resource  need to wait for previous instruction to complete so to use the resource
Data hazard
  Need to wait for previous instruction to complete its data read/write so to use the storage (registers/memory)
Control hazard
  Need to wait for previous control-flow instruction to complete to decide whether to execution
Can always resolve hazards by waiting
  Pipeline control must detect the hazard
  Take action (or delay action) to resolve hazards

## Slide 5: Structure Hazards
Suppose RISC-V pipeline has only a single memory
  Load/store requires data access at its MEM stage
  The third following instruction in IF also requires memory
Mem
I
n
s
t
r.
O
r
d
e
r
Time
ld
Instr 1
Instr 2
Instr 3
Instr 4
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
Both instructions access memory at same cycle

## Slide 6: Structure Hazards
Suppose RISC-V pipeline has only a single memory
  The third following instruction would have to stall for that cycle  cause a pipeline “bubble”
Solution: use two memory (data, instruction memory)
  Or separate instruction/data caches
I-Mem
ALU
Reg
D-Mem
Reg

## Slide 7: Data Hazards
An instruction depends on completion of data access to the same register by a previous instruction add x19, x0, x1 sub x2, x19, x3
  Their overlapped execution in pipeline would cause the dependent instruction to fetch wrong data in registers
Time
add x19,x0,x1
sub x2,x19,x3
ALU
IM
Reg
DM
Reg
ALU
IM
DM
Reg
Reg

## Slide 8: Dependences and Data Hazards
Data dependences between instructions may cause data hazards, depending on relative positions in pipe
RAW (read after write):
  sub x2,x1,x3 and x6,x2,x5
WAR (write after read):
  sub x6,x2,x5 and x2,x1,x3
WAW (write after write):
  sub x2,x1,x3 and x2,x6,x5
i2 tries to read operand in the pipeline before i1 writes it  get old data instead of new
i2 tries to write operand in the pipeline before i1 reads it  get new data instead of old
i2 tries to write operand in the pipeline before i1 writes it  leave wrong data

## Slide 9: Data Hazards in RISC-V 5-Stage Pipeline
WAR (write after read) and WAW (write after write) can’t happen in RISC-V 5-stage pipeline because:
  All instructions take 5 stages
  Reads are always in stage 2
  Writes are always in stage 5
Thanks to the regularity in RISC-V ISA design
But, we still need to resolve RAW hazards
  RAW hazards may occur between different stages

## Slide 10: RAW Hazards among Different Stages
sub x2,x1,x3 and x12,x2,x5 or x13,x6,x2 add x14,x2,x2 sw x15,100(x2)
No hazard:
Write in 1st half cycle & read in 2nd half
Fig. 4.50
X2 = 10
X2 = -20

## Slide 11: Resolving Data Hazards
Let dependent instruction wait until hazard is resolved, i.e., stall i2 until i1 writes back to register at the WB stage  insert pipeline bubbles
Better: forward data as soon as it is computed

## Slide 12: Forwarding (Bypassing)
Use result when it is computed, e.g., by ALU at the EX stage
  Don’t wait for it to be stored in a register at WB stage
  Requires extra connections in the datapath
X

## Slide 13: Forwarding between Stages
No hazard
Fig. 4.51

## Slide 14: Detecting the Need to Forward
Rs1
Rs2
Rd
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs1 = register number for Rs1 sitting in ID/EX pipeline register
ALU operand register numbers in EX stage given by
  ID/EX.RegisterRs1, ID/EX.RegisterRs2
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs1 or
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRs2
Fwd from EX/MEM pipeline reg

## Slide 15: Detecting the Need to Forward
Data hazards when (cont.)
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs1
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRs2
Fwd from MEM/WB pipeline reg
Rs1
Rs2
Rd

## Slide 16: Detecting the Need to Forward
But data hazard will occur only if the forwarding instruction will write to a register!
  EX/MEM.RegWrite (for EX/MEM to ID/EX)
  MEM/WB.RegWrite (for MEM/WB to ID/EX)
And only if Rd for that instruction is not x0
  EX/MEM.RegisterRd ≠ 0 (for EX/MEM to ID/EX)
  MEM/WB.RegisterRd ≠ 0 (for MEM/WB to ID/EX)

## Slide 17: Forwarding Paths
Rd
EX hazard
Fig. 4.52

## Slide 18: Forwarding Conditions
EX hazard
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs1)) ForwardA = 10
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs2)) ForwardB = 10

## Slide 19: Forwarding Paths
Rd
MEM hazard
Fig. 4.52

## Slide 20: Forwarding Conditions
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRs1)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRs2)) ForwardB = 01
But there is a problem …

## Slide 21: Double Data Hazards
Consider the sequence:
  add x1,x1,x2 sub x1,x1,x3 and x1,x1,x4
Both hazards occur and both add and sub want to forward to and  use the most recent, i.e., sub
Thus, need to revise MEM hazard condition
  Forward only if EX hazard condition isn’t true

## Slide 22: Revised Forwarding Condition
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs1)) and (MEM/WB.RegisterRd = ID/EX.RegisterRs1)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs2)) and (MEM/WB.RegisterRd = ID/EX.RegisterRs2)) ForwardB = 01

## Slide 23: Datapath with Forwarding
Fig. 4.54

## Slide 24: Can't Always Forward
ld can still cause a hazard: (load-use data hazard)
  If it is followed by an instruction to read the loaded reg.
Need to stall for one cycle
Fig. 4.56
ld x2,20(x1)
and x4,x2,x5

## Slide 25: Load-Use Hazard Detection
Check when the using instruction is decoded in the ID stage (lw is in the EX stage)
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRs1, IF/ID.RegisterRs2
Load-use hazard when
  ID/EX.MemRead and ((ID/EX.RegisterRd = IF/ID.RegisterRs1) or (ID/EX.RegisterRd = IF/ID.RegisterRs2))
  Note that ID/EX.MemRead=1 indicates a load instruction
If detected, stall and insert bubble

## Slide 26: How to Stall an Instruction in the Pipeline?
Stall pipeline by keeping instructions in same stage and inserting an NOP instead
Stall inserted here
Fig. 4.57

## Slide 27: How to Stall the Pipeline?
Stall instructions in IF and ID: Prevent update of PC and IF/ID register
  The using instruction is decoded again
  The following instruction is fetched again
  1-cycle stall allows MEM to read data for ld
    Can subsequently forward to EX stage
What to move into EX: Force control signals in ID/EX register to 0
  Turn EX, MEM and WB into NOP (no-operation)
  As control signals propagate, all control signals to EX, MEM, WB are deasserted, no registers or memories are written

## Slide 28: Datapath with Stalling Unit
Fig. 4.58
Prevent update of PC & IF/ID
Force control values in ID/EX to 0
ID/EX.MemRead and ((ID/EX.Rt = IF/ID.Rs1) or (ID/EX.Rt = IF/ID.Rs2))

## Slide 29: Stalls and Performance
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure
C code for A = B + E; C = B + F;
ld x1, 0(x0)
ld x2, 8(x0)
add x3, x1, x2
sd x3, 24(x0)
ld x4, 16(x0)
add x5, x1, x4
sd x5, 32(x0)
stall
stall
ld x1, 0(x0)
ld x2, 8(x0)
ld x4, 16(x0)
add x3, x1, x2
sd x3, 24(x0)
add x5, x1, x4
sd x5, 32(x0)
11 cycles
13 cycles

## Slide 30: Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
  Need to wait until branch outcome determined before fetching next instruction
In RISC-V pipeline
  Need to compare registers and compute target early in the pipeline
  How early can we do it in the pipeline?

## Slide 31: Control Hazards
beq determines whether to branch at the MEM stage
beq

## Slide 32: Control Hazards
When beq decides to branch, the following 3 instructions are already in pipeline!
PC
Flush these instructions
(Set control values to 0)
Fig. 4.59

## Slide 33: Reducing Branch Delay
Add hardware to determine outcome at ID stage
  Check branch equality at ID (using XOR)
  Target address adder at ID stage
  Will still fetch the next sequential instruction  add a control signal, IF.Flush, to zero instruction field of IF/ID (making the following instruction an NOP)
Example: branch taken
  36: sub x10, x4, x8 40: beq x1, x3, 16 // branch to 40+16*2=72 44: and x12, x2, x5 48: or x13, x2, x6 52: add x14, x4, x2 56: sub x15, x6, x7 ... 72: ld x4, 50(x7)

## Slide 34: Example: Branch Taken
Fig. 4.60

## Slide 35: Example: Branch Taken
Fig. 4.60

## Slide 36: Example: Branch Taken
Fig. 4.60

## Slide 37: Data Hazards for Branches
If a comparison register is a destination of 2nd or 3rd preceding ALU instruction
Can resolve using forwarding (how?)
  Need to forward to ID stage in addition to EX stage!
…
add x4,x5,x6
add x1,x2,x3
beq x1,x4,target
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB

## Slide 38: Data Hazards for Branches
If a comparison register is a destination of preceding ALU instruction or 2nd preceding load instruction
  Need 1 stall cycle
beq stalled
add x4,x5,x6
ld x1,addr
beq x1,x4,target
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
ID
EX
MEM
WB

## Slide 39: Data Hazards for Branches
If a comparison register is a destination of immediately preceding load instruction
  Need 2 stall cycles
How to check the conditions and stall pipeline stage?
beq stalled
IF
ID
EX
MEM
WB
IF
ID
ID
ID
EX
MEM
WB
beq stalled
ld x1,addr
beq x1,x0,target

## Slide 40: Handling Control Hazards
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Option 1: dynamic branch prediction
  Predict outcome of branch
  Only stall if prediction is wrong
Option 2: compiler rescheduling

## Slide 41: Branch Prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop and if-statement branches
    Predict backward branches taken
    Predict forward branches not taken
  In RISC-V pipeline, can predict branches always not taken
    Fetch instruction after branch, with no delay
  Need to add hardware for flushing instructions if wrong
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history

## Slide 42: Dynamic Branch Prediction
Need to prediction two things:
  Branch direction
  Branch target
Branch direction:
  Branch prediction buffer (branch history table), indexed by recent branch instruction addresses
  Stores outcome (taken/not taken) in the table
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 43: Predicting Branch Direction
Predict branch based on past history of branch
Branch History Table (BHT)
PC
.
.
.
.
.
2N entries
Prediction
N bits
FSM
Update
Logic
Table update
Actual outcome
BHT: a cache of recent branches
Each entry stores last direction that the indexed branch went (1 bit to encode taken/not-taken)
No need to decode to know if it is a branch, just look at instr. address
Hash
Notes: Branch History Table (BHT)
Indexed by PC (or fraction of it)
Each entry stores last direction that the indexed branch went (1 bit to encode taken/not-taken)
Table is a cache of recent branches; non-branch instructions will have an entry of not-taken causing IF to fetch from sequential
Buffer size of 4096 entries are common (track 4K different branches)
When branch direction is resolved, go back into the table and update entry: 0 if not taken, 1 if taken

## Slide 44: Problem with 1-Bit Predictor
Inner loop branches mispredicted twice!
  Mispredict as taken on last iteration of inner loop
  Then mispredict as not taken on first iteration of inner loop next time around
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer

## Slide 45: Solution: 2-Bit Predictor
Change prediction on two successive mispredictions
Fig. 4.61

## Slide 46: Calculating the Branch Target
Need target address at same time as prediction
  Branch Target Buffer (BTB): use PC to fetch instruction and simultaneously look up BTB to get prediction AND branch address (if taken)
Branch PC
Predicted PC
=?
PC of instruction
Fetch
Yes: instruction is branch and use predicted PC as next PC
No: branch not predicted, proceed normally
Branch predicted
taken or untaken

## Slide 47: Outline
Problem statement and logic review (Sec. 4.1, 4.2)
Building a simple RISC-V processor with datapath and control (Sec. 4.3, 4.4)
Building a pipelined RISC-V processor with datapath and control (Sec. 4.5, 4.6)
Dealing hazards in pipelined processor: data and control hazards (Sec. 4.7, 4.8)
Handling exceptions (Sec. 4.9)
More advanced topics: parallelism via instructions, ARM Cortex-A53 and Intel Core i7 Pipelines, instruction-level parallelism (Sec. 4.10, 4.11, 4.12)

## Slide 48: Events and Interrupts
What happen if CPU fetches an instruction and cannot understand its opcode?
What happen if you type a key on the keyboard? How does the computer know and start processing your input?
When these special “events” occur, the CPU needs to “interrupt” the currently executing program and switch to execute some special subroutines to handle the events

## Slide 49: Exceptions and Interrupts
“Unexpected” events requiring change in flow of control to service the events
  Similar to a procedure call, but unplanned
Exception
  Arises within CPU, e.g., undefined opcode, overflow, syscall
Interrupt
  From an external I/O controller

## Slide 50: Detection of Exceptions and Interrupts
How does the CPU know when there is an interrupt?
  Usually when it receives a signal from one of the IRQ (interrupt request) pins, which are connected to one or more external I/O controllers
How about exceptions?
  CPU controller may raise a flag, e.g., undefined opcode, overflow, …

## Slide 51: Handling External Interrupts
What does the CPU do in handling an interrupt?
  When receiving an interrupt signal, the CPU (1) stops at the next instruction (2) saves the address of the next instruction somewhere (3) jumps to a specific interrupt service routine (ISR) or interrupt handler
  ISR is basically a subroutine (stored at some specific location in memory) to perform operations to handle the interrupt with a RETURN at the end
How to be transparent to the running program?
  Similar to handling a procedure call

## Slide 52: Interrupt Service Routine
The following shows an example of an ISR
      Task Code ISR
        ...
        ld x3,100(x9)
        or x1,x3,x4 sd x3,0(sp)
        add x4,x2,x3 sd x4,-4(sp)
        and x2,x3,x5 ...
        beq x7,x9,END ;ISR code using x3,x4
        sub x1,x3,x4 ...
        ... ld x4,-4(sp)
        ... ld x3,0(sp)
    END: add x7,x8,x1 return
        ... ...
Save & restore (partial)
program state

## Slide 53: Handling Internal Exceptions in RISC-V
Save PC of offending instruction
  In RISC-V: Supervisor Exception Program Counter (SEPC)
Save indication of the problem
  In RISC-V: Supervisor Exception Cause Register (SCAUSE)
  64 bits, but most bits unused
    Exception code field: 2 for undefined opcode, 12 for hardware malfunction, …
  CPU controller will supply this based on exception
Jump to interrupt handler in OS to handle the exception based on the cause
  Assume at 0000 0000 1C09 000016 (single entry point for all exceptions)

## Slide 54: OS Handling Exceptions in RISC-V
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  Use SEPC to return to program
Otherwise
  Terminate program
  Report error using SEPC, SCAUSE, …

## Slide 55: Alternate Way to Indicate Cause
Different handlers handle different causes/interrupts
  Handler’s address in memory determined by the cause  vectored Interrupts
An exception vector address, supplied by the CPU controller based on interrupt source, to be added to a vector table base register to give handler address
  Undefined opcode: 00 0100 00002
  Hardware malfunction: 01 1000 00002
  …: …
Instructions inside the handler either
  Deal with the interrupt, or
  Jump to the real handler
Exception vector address to be added to a Vector Table Base Register,

## Slide 56: Exceptions in a RISC-V Pipeline
Treated as another form of control hazard
Consider malfunction on add in EX stage
  add x1, x2, x3
  Must prevent x1 from being clobbered
  (1) Complete previous instructions
  (2) Flush add and subsequent instructions, IF.Flush, ID.Flush, EX.Flush
  (3) Set SEPC and SCAUSE register values
  (4) Transfer control to handler at 0000 0000 1C09 000016
Similar to mispredicted branch
  Use much of the same hardware

## Slide 57: Pipeline with Exceptions
Fig. 4.63
Notes: The ALU overflow signal is an input to the control unit.

## Slide 58: Exception Handling
Restartable exceptions
  Pipeline flushes the offending instruction and following instructions
  Handler executes and then returns to the instruction
    The instruction is refetched and executed from scratch
PC saved in SEPC register
  Identifies the instruction causing the exception

## Slide 59: Exception Example
Exception on add in
  40 sub x11, x2, x4 44 and x12, x2, x5 48 or x13, x2, x6 4C add x1, x2, x1 50 sub x15, x6, x7 54 ld x16, 50(x7) …
Handler
  1C090000 sd x26, 1000(x0) 1C090004 sd x27, 1008(x0) …

## Slide 60: Exception Example
Fig. 4.64
malfunction

## Slide 61: Exception Example
Fig. 4.64

## Slide 62: Multiple Exceptions
Pipelining overlaps multiple instructions
  Could have multiple exceptions at once
Simple approach:
  Deal with exception from earliest instruction
  Flush subsequent instructions  “precise” exceptions
  Good to know in which pipeline stage a type of exception can occur
In complex pipelines
  Multiple instructions per cycle, out-of-order completion
  Maintaining precise exceptions is difficult!
Some computers provide imprecise exceptions
  Simplifies hardware, but more complex handler software
Notes: Just stop pipeline and save state
  Including exception cause(s)
Let the handler work out
  Which instruction(s) had exceptions
  Which to complete or flush
    May require “manual” completion

## Slide 63: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
  Handling hazards by forwarding, stalling, compiler scheduling
Must handle exceptions properly
Instruction set design affects complexity of pipeline implementation

## Slide 64: Backup Slides

## Slide 65: Outline
Problem statement and logic review (Sec. 4.1, 4.2)
Building a simple RISC-V processor with datapath and control (Sec. 4.3, 4.4)
Building a pipelined RISC-V processor with datapath and control (Sec. 4.5, 4.6)
Dealing hazards in pipelined processor: data and control hazards (Sec. 4.7, 4.8)
Handling exceptions (Sec. 4.9)
More advanced topics: parallelism via instructions, ARM Cortex-A53 and Intel Core i7 Pipelines, instruction-level parallelism (Sec. 4.10, 4.11, 4.12)

## Slide 66: Instruction-Level Parallelism (ILP)
Pipelining: execute multiple instructions in parallel
To increase ILP:
  Deeper pipeline  less work per stage, shorter clock cycle
    Still one cycle per instruction
  Multiple-issue
    Replicate pipeline stages  multiple pipelines
    Fetch and start multiple instructions per clock cycle
    CPI < 1, e.g., 4GHz 4-way multiple-issue  16 BIPS, peak CPI = 0.25, peak IPC = 4 (Instructions Per Cycle)  dependencies among instructions reduce this in practice

## Slide 67: Multiple Issue
Static multiple issue
  Compiler detects and avoids hazards, and groups parallel instructions to be issued together
  Packages them into “issue slots”  very long instruction word (VLIW)
  CPU does not need to check hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue in each cycle (limited by instruction fetch window)
  Compiler can help by reordering instructions so that CPU may find more parallel instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 68: Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome
    Roll back if path taken is different
  Speculate on load
    Roll back if location is updated

## Slide 69: Compiler/Hardware Speculation
Compiler can reorder instructions
  e.g., move load before branch
  Can include “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until it determines they are actually needed
  Flush buffers on incorrect speculation

## Slide 70: Speculation and Exceptions
What if exception occurs on a speculatively executed instruction?
  e.g., speculative load before null-pointer check
Static speculation
  Can add ISA support for deferring exceptions
Dynamic speculation
  Can buffer exceptions until instruction completion (which may not occur)

## Slide 71: Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
   Very Long Instruction Word (VLIW)

## Slide 72: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies with a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nop if necessary

## Slide 73: RISC-V with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 74: RISC-V with Static Dual Issue

## Slide 75: Hazards in the Dual-Issue RISC-V
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    add x10, x0, x1 ld x2, 0(x10)
    Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling required

## Slide 76: Scheduling Example
Schedule this for dual-issue RISC-V
  IPC = 5/4 = 1.25 (c.f. peak IPC = 2)
Loop: ld x31,0(x20) // x31=array element add x31,x31,x21 // add scalar in x21 sd x31,0(x20) // store result addi x20,x20,-8 // decrement pointer blt x22,x20,Loop // branch if x22 < x20
 | ALU/branch | Load/store | cycle
Loop: | nop | ld x31,0(x20) | 1
 | addi x20,x20,-8 | nop | 2
 | add x31,x31,x21 | nop | 3
 | blt x22,x20,Loop | sd x31,8(x20) | 4

## Slide 77: Loop Unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
Use different registers per replication
  Called “register renaming”
  Avoid loop-carried “anti-dependencies”
    Store followed by a load of the same register
    Aka “name dependence”: reuse of a register name

## Slide 78: Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2, but at cost of registers and code size
 | ALU/branch | Load/store | cycle
Loop: | addi x20,x20,-32 | ld x28, 0(x20) | 1
 | nop | ld x29, 24(x20) | 2
 | add x28,x28,x21 | ld x30, 16(x20) | 3
 | add x29,x29,x21 | ld x31, 8(x20) | 4
 | add x30,x30,x21 | sd x28, 32(x20) | 5
 | add x31,x31,x21 | sd x29, 24(x20) | 6
 | nop | sd x30, 16(x20) | 7
 | blt x22,x20,Loop | sd x31, 8(x20) | 8

## Slide 79: Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 80: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  ld x31,20(x21) add x1,x31,x2 sub x23,x23,x3 andi x5,x23,20
  Can start sub while add is waiting for ld

## Slide 81: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands

## Slide 82: Register Renaming
Reservation stations and reorder buffer effectively provide register renaming
On instruction issue to reservation station
  If operand is available in register file or reorder buffer
    Copied to reservation station
    No longer required in the register; can be overwritten
  If operand is not yet available
    It will be provided to the reservation station by a function unit
    Register update may not be required

## Slide 83: Speculation
Predict branch and continue issuing
  Don’t commit until branch outcome determined
Load speculation
  Avoid load and cache miss delay
    Predict the effective address
    Predict loaded value
    Load before completing outstanding stores
    Bypass stored values to load unit
  Don’t commit load until speculation cleared

## Slide 84: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g., cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards

## Slide 85: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g., pointer aliasing
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well

## Slide 86: Power Efficiency
Complexity of dynamic scheduling and speculations requires power
Multiple simpler cores may be better
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
UltraSparc III | 2003 | 1950MHz | 14 | 4 | No | 1 | 90W
UltraSparc T1 | 2005 | 1200MHz | 6 | 1 | No | 8 | 70W

## Slide 87: Fallacies
Pipelining is easy (!)
  The basic idea is easy
  The devil is in the details
    e.g., detecting data hazards
Pipelining is independent of technology
  So why haven’t we always done pipelining?
  More transistors make more advanced techniques feasible
  Pipeline-related ISA design needs to take account of technology trends
    e.g., predicated instructions

## Slide 88: Pitfalls
Poor ISA design can make pipelining harder
  e.g., complex instruction sets (VAX, IA-32)
    Significant overhead to make pipelining work
    IA-32 micro-op approach
  e.g., complex addressing modes
    Register update side effects, memory indirection
  e.g., delayed branches
    Advanced pipelines have long delay slots