## Slide 1: CS4100: Computer Architecture Memory Hierarchy (I)
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Outline
Introduction to memory hierarchy (Sec. 5.1)
Memory technologies (Sec. 5.2, 5.5)
Caches (Sec. 5.3, 5.4, 5.9)
Virtual memory (Sec. 5.7)
Framework for memory hierarchy (Sec. 5.8)
Virtual machines (Sec. 5.6)
Parallelism and memory hierarchies: cache coherence, redundant arrays of inexpensive disks (Sec. 5.10, 5.11)

## Slide 3: Why Memory Hierarchy?
Programmers want unlimited amounts of memory with low latency
  But fast memory more expensive than slower memory
Solution: small fast memory + big slow memory = Looks like a big fast memory
MC
Small and fast
MM
Big and slow
Big
Fast
Notes: Why does this work?

## Slide 4: How to Use Memory Hierarchy?
Entire addressable memory space available in largest, slowest memory
  Incrementally smaller and faster memories, each containing a subset of the memory below it, proceed toward processor
  Upper level: closer to processor (smaller, faster, expensive)
  Lower level: away from processor (bigger, slower, cheap)
Control
Datapath
Secondary
Storage
(Disk)
Processor chip
Registers
L2
Cache
Main
Memory
(DRAM)
On-Chip
Cache

## Slide 5: Why Memory Hierarchy Works?
Principle of locality:
  Programs access a small proportion of their address space (data and instruction) at any time  a program property
Two types of locality:
  Temporal locality: items accessed recently are likely to be accessed again soon, e.g., instructions in a loop
  Spatial locality: items near those accessed recently are likely to be accessed soon, e.g., sequential instruction access, array data
Prob.
Location
Code
Stack
Array
Prob.
time

## Slide 6: How Does It Work?
Temporal locality: keep most recently accessed data items closer to the processor (faster reuse)
Spatial locality: move blocks consisting of contiguous words to the upper levels (bring in neighbors)
Block (or page): basic unit of data transfer
  Minimum unit of data that can either be present or not present in a level of the hierarchy
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Block Y
Notes: The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in details in the next lecture on caches).
+1 = 16 min. (X:56)

## Slide 7: Levels of Memory Hierarchy
CPU
Registers
Cache
Memory
Disk
CPU Registers
100s Bytes <1s cycle
Cache
M Bytes
10s cycles
Main Memory
G Bytes
100s cycles
Disk
T Bytes
1M cycles
Capacity
Access Time
Instr. operands
Blocks
Pages
Management
Unit
prog./compiler
1-8 bytes
cache controller
8-128 bytes
OS
512-1M bytes
Upper Level
Lower Level
faster
Larger

## Slide 8: Hit or Miss
Hit: accessed data appears in upper level
  Hit rate: % of memory accesses found in upper level
  Hit time: time to access upper level
Miss: data not in upper level
  Miss rate = 1 - (hit rate)
  Miss penalty: time to replace a block in upper level + time to deliver the block to the processor
Hit Time << Miss Penalty
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Blk X
Blk Y
miss
Notes: A HIT is when the data the processor wants to access is found in the upper level (Blk X).
The fraction of the memory access that are HIT is defined as HIT rate.
HIT Time is the time to access the Upper Level where the data is found (X). It consists of:
(a) Time to access this level.
(b) AND the time to determine if this is a Hit or Miss.
If the data the processor wants cannot be found in the upper level, then we have a miss and we need to retrieve the data (Blk Y) from the lower level.
By definition (definition of Hit: Fraction), the miss rate is just 1 minus the hit rate.
This miss penalty also consists of two parts:
(a) The time it takes to replace a block (Blk Y to BlkX) in the upper level.
(b) And then the time it takes to deliver this new block to the processor.
It is very important that your Hit Time to be much much smaller than your miss penalty. Otherwise, there will be no reason to build a memory hierarchy.
+2 = 14 min. (X:54)

## Slide 9: 4 Questions for Memory Hierarchy Design
Q1: Where can a block be placed in the upper level?
  One fixed location, a few locations, anywhere
Q2: How is a block found if it is in the upper level?
  Depending on strategy taken in Q1
  Indexing, table lookup, parallel search
Q3: Which block should be replaced on a miss?
  Ideal: one that not to be used in the farthest future
  Practical: use the past to predict the future  how to “track” the past?
Q4: What happens on a write?
  Write to upper level only or to lower level as well
  What if write miss?

## Slide 10: Summary of Memory Hierarchy
Two different types of locality:
  Temporal locality (locality in time)
  Spatial locality (locality in space)
Using the principle of locality:
  Present the user/program with as much memory as is available in the cheapest technology
  Provide access at the speed offered by the fastest memory
End result: provide user/program an illusion of a big fast random access memory
Notes: The first thing we covered is the principle of locality.
There are two types of locality: temporal, or locality of time and spatial, locality of space.
We talked about memory system design.
The key idea of memory system design is to present the user with as much memory as possible in the cheapest technology while by taking advantage of the principle of locality, create an illusion that the average access time is close to that of the fastest technology.
As far as Random Access technology is concerned, we concentrate on 2: DRAM and SRAM.
DRAM is slow but cheap and dense so is a good choice for presenting the use with a BIG memory system.
SRAM, on the other hand, is fast but it is also expensive both in terms of cost and power, so it is a good choice for providing the user with a fast access time.
+2 = 78 min. (Y:58)

## Slide 11: Outline
Introduction to memory hierarchy (Sec. 5.1)
Memory technologies (Sec. 5.2, 5.5)
  Dependable memory hierarchy (Sec. 5.5)
Caches (Sec. 5.3, 5.4, 5.9)
Virtual memory (Sec. 5.7)
Framework for memory hierarchy (Sec. 5.8)
Virtual machines (Sec. 5.6)
Parallelism and memory hierarchies: cache coherence, redundant arrays of inexpensive disks (Sec. 5.10, 5.11)

## Slide 12: Memory Technology
Random access: access time same for all locations
  Can access any random location at any time
SRAM: Static Random Access Memory
  Store bits like a flip-flop  content will last until lose power
  Low density, high power, expensive, fast
  Used for caches
DRAM: Dynamic Random Access Memory
  Store bits in capacitor charges  charges will leak and eventually disappear  dynamic
  High density, low power, cheap, slow
  Used for main memory
Word Line (Control)
Storage Capacitor
Bit Line (Data)
Notes: The technology we used to build our memory hierarchy can be divided into two categories: Random Access and Non-so-Random Access.
Because random access means you can access any random location at any time and the access time will be the same as any other random locations.
Which is NOT the case for disks or tape where the access time for a given location at any time can be quite different from some other random locations at some other random time.
As far as Random Access technology is concerned, we will concentrate on two specific technologies: Dynamic RAM and Static RAM.
The advantages of Dynamic RAMs are high density, low cost, and low power so we can have a lot of them without burning a hole in our budget or our desktop.
The disadvantages of DRAM are they are slow. Also they will forget what you tell them if you don remind them constantly (Refresh). We will talk more about refresh later today.
SRAM only has one redeeming feature: it is fast. Other than that, they have low density, expensive, and burn a lot of power. Oh, SRAM actually has another redeeming feature. They will not forget what you tell them. They will keep whatever you write to them forever.
Well orever?is a long time. So lets just say it will keep your data as long as you don pull the plug on your computer.
In the next two lectures, we will be focusing on DRAMs and SRAMs.
We will not get into disk until the Virtual Memory lecture a week from now.
+3 = 19 min. (X:59)

## Slide 13: Comparisons of Memory Technologies
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk
Memory technology | Typical access time | $ per GB in 2008
SRAM | 0.5 ~ 2.5 ns | $2000 ~ $5,000
DRAM | 50 ~ 70 ns | $20 ~ $75
Magnetic disk | 5 ~ 20 ms | $0.20 ~ $2

## Slide 14: DRAM Technology
Data stored as a charge in a capacitor
  Single transistor used to access the charge
  Destructive read and need to write back
  Bits are organized as a rectangular array
    An entire row is accessed into a row buffer
  Must periodically be refreshed
    Read contents and write back
    Performed on a DRAM row
Word Line (Control)
Storage Capacitor
Bit Line (Data)
Row buffer
wordline
bitline
Row addr decoder
Col. addr
decoder
Data out
Address
Row addr
Col. addr

## Slide 15: Advanced DRAM Organizations
Burst mode:
  Supply successive words from row buffer  reduce latency
Synchronous DRAM:
  Clocking DRAM interface for repeated transfers without handshaking overhead
Double data rate (DDR) DRAM
  Transfer on rising and falling clock edges
DRAM banking:
  Multiple DRAM banks allowing simultaneous accesses (next slide)
https://en.wikipedia.org/wiki/Double_data_rate

## Slide 16: DRAM Banking
One memory bank
Four interleaved memory banks
  Pipelined access for increased bandwidth
Memory Bank Cycle Time
CPU
Memory
CPU
Memory bank 1
Memory bank 2
Memory bank 0
Memory bank 3
https://people.rit.edu/meseec/cmpe550-spring2018/

## Slide 17: Flash Storage
Nonvolatile semiconductor storage
  100× ~ 1000× faster than disk
  Smaller, lower power, more robust, more $/GB
  Store bits in floating-gate transistors
  Apply a voltage VT1< V < VT2 to CG: if transistor on  FG uncharged  a logic “1” is stored
(By Cyferz at English Wikipedia, CC BY 2.5, https://commons.wikimedia.org/w/index.php?curid=47813471)
Floating gate (FG) traps charges and changes threshold voltage (VT1VT2) at control gate (CG) to turn on transistor
Notes: In order to read a value from the transistor, an intermediate voltage between the threshold voltages (VT1 & VT2) is applied to the CG. If the channel conducts at this intermediate voltage, the FG must be uncharged (if it was charged, we would not get conduction because the intermediate voltage is less than VT2), and hence, a logical "1" is stored in the gate. If the channel does not conduct at the intermediate voltage, it indicates that the FG is charged, and hence, a logical "0" is stored in the gate.

## Slide 18: Flash Storage
NOR flash: bit cell like a NOR gate
  Random read/write access
  Used for instruction memory in embedded systems
NAND flash: bit cell like a NAND gate
  Denser and cheaper, block-at-a-time access
  Used for USB keys, media storage, …
Flash bits wears out after 1000’s of accesses
  Wear leveling: remap data to less used blocks
L
H’
L
X
_
X
H
H’
H
H
H
|
|
|
|
|
Notes: In NOR Flash, cells are connected in parallel to the bit lines, which allow the cells to be read and programmed individually. NOR flash acts like a NOR gate, when one of the word lines (connected to the cell's CG) is brought high, the corresponding storage transistor acts to pull the output bit line low. A NOR flash cell can be programmed, or set to a binary "0" value, by the following procedure:
* an elevated on-voltage (typically >5 V) is applied to the CG
* the channel is now turned on, so electrons can flow from the source to the drain (assuming an NMOS transistor)
* the source-drain current is sufficiently high to cause some high energy electrons to jump through the insulating layer onto the FG, via a process called hot-electron injection.
In NAND Flash, the cells are connected in series, resembling a NAND gate: several transistors are connected in series, and the bit line is pulled low only if all the word lines are pulled high (above the transistors' VT). These groups are then connected via some additional transistors to a NOR-style bit line array in the same way that single transistors are linked in NOR flash. The series connections consume less space than the parallel ones, reducing the cost of NAND Flash. It does not, by itself, prevent NAND cells from being read and programmed individually. (https://www.researchgate.net/figure/Comparison-of-NOR-Flash-array-and-NAND-Flash-array-architectures_fig8_265727614)

## Slide 19: Disk Storage
Nonvolatile, rotating magnetic storage
Actuator
Arm
Head
Platters
Spindle

## Slide 20: Disk Sectors and Access
Each sector records
  Sector ID
  Data (512 bytes, 4096 bytes proposed)
  Error correcting code (ECC)
    Used to hide defects and recording errors
  Synchronization fields and gaps
Access to a sector involves
  Queuing delay: if other accesses are pending
  Seek time: time to move the heads to desired track
  Rotational latency: time for desired sector under head
  Data transfer: time to transfer desired sector
  Controller overhead
Sector
Track
Cylinder
Head
Platter

## Slide 21: Disk Access Example
Given
  512B sector, 15,000rpm, 4ms average seek time, 100MB/s transfer rate, 0.2ms controller overhead, idle disk
Average read time
  4ms seek time + ½ / (15,000/60) = 2ms rotational latency + 512 / 100MB/s = 0.005ms transfer time + 0.2ms controller delay = 6.2ms
If actual average seek time is 1ms
  Average read time = 3.2ms

## Slide 22: Outline
Introduction to memory hierarchy (Sec. 5.1)
Memory technologies (Sec. 5.2, 5.5)
  Dependable memory hierarchy (Sec. 5.5)
Caches (Sec. 5.3, 5.4, 5.9)
Virtual memory (Sec. 5.7)
Framework for memory hierarchy (Sec. 5.8)
Virtual machines (Sec. 5.6)
Parallelism and memory hierarchies: cache coherence, redundant arrays of inexpensive disks (Sec. 5.10, 5.11)

## Slide 23: Is Your Memory Reliable?
What is failure?
  Given a specification of proper service (of memory)
  Fault: failure of a component, may or may not cause failure
Service accomplishment
Service delivered as specified
Service interruption
Deviation from specified service
Failure
Restoration
Failure may be permanent or intermittent

## Slide 24: Reliability vs. Availability
Reliability: a measure of continuous service accomplishment (or the time to failure), starting from a reference point
  Mean time to failure (MTTF): a reliability measure
  Mean time to repair (MTTR): a measure of service interruption
  Mean time between failures (MTBF): = MTTF + MTTR
Availability: a measure of service accomplishment with respect to the alternation between the two states of accomplishment and interruption
  Availability = MTTF / (MTTF + MTTR)

## Slide 25: Reliability vs. Availability
We want high availability (HA)
  Can be expressed as # of “nines of availability” per year
    One nine: 90%  36.5 days of repair/year
    Five nines: 99.999%  5.26 minutes of repair/year
HA can be achieved by
  Reducing MTTR: improved tools and processes for fault detection, diagnosis and repair
  Increasing MTTF: improve quality of components or design systems to continue operation in the presence of components that have failed
    Fault avoidance: reliable components
    Fault tolerance: redundant components
    Fault forecasting: predict and replace before failure

## Slide 26: Fault Tolerance for Memory
Hamming Single Error Correcting, Double Error Detecting Code (SECDED)
Hamming distance:
  Minimum number of bits that are different between any two correct bit patterns
    A measure of how “close” correct bit patterns can be
    e.g., Hamming distance between 011011 and 001111 is two
Single Error Detecting Code:
  A set of legal bit patterns that can detect single bit error
00
01
11
10
Notes: Richard Hamming

## Slide 27: Single Error Detecting Code
The simplest way to encode four different things:
  Suppose you send the code “01” to ask your friend to bring you a banana, but the code was erroneously transmitted as “11”  Can she/he tell there is a bit error?
  How about this code?
 00
 01
 11
 10
 000
 011
 110
 101
Why it works?
Notes: the parity of the N+1 bit word should always be even

## Slide 28: Single Error Detecting Code
Hamming distance of 3-bit codes
  A link between two codes whose Hamming distance = 1
Single Error Detecting Code:
  Condition: if only every pair of legal bit patterns has a Hamming distance of 2, e.g., parity code
100
101
111
110
000
001
011
010
Legal bit patterns are actually
original codes (00, 01, 10, 11) plus even parity (bit 0)
But, which bit is in error?

## Slide 29: Single Error Correcting (SEC) Code
A code with a Hamming distance of 3 provides single error correction (Why?)
100
101
111
110
000
001
011
010

## Slide 30: Single Error Correcting (SEC) Code
Hamming Error Correction Code (ECC):
  Number bits from 1 on the left
  All bit positions that are a power 2 are parity bits
  Each parity bit checks group of data bits via even parity:
Fig. 5.24
Notes: ■ Bit 1 (0001two) checks bits (1,3,5,7,9,11,...), which are bits where rightmost bit of address is 1 (0001two, 0011two, 0101two, 0111two, 1001two, 1011two,…).
■ Bit 2 (0010two) checks bits (2,3,6,7,10,11,14,15,…), which are the bits where the second bit to the right in the address is 1.
■ Bit 4 (0100two) checks bits (4–7, 12–15, 20–23,...) , which are the bits where the third bit to the right in the address is 1.
■ Bit 8 (1000two) checks bits (8–15, 24–31, 40–47,...), which are the bits where the fourth bit to the right in the address is 1.

## Slide 31: Single Error Correcting (SEC) Code
Sum of positions of erroneous parity bits identifies the erroneous bit, e.g.,
  Erroneous parity bits = 0000 indicates no error
  Erroneous parity bits = 1001  bit 1+8=9 was flipped
Example 1:
  Encode 100110102  _ _ 1 _ 0 0 1 _ 1 0 1 0?
    Position 1 should make bits 1, 3, 5, 7, 9, 11 even parity _ _ 1 _ 0 0 1 _ 1 0 1 0  p1 = 0
  Final code word = 011100101010
  If we detect bit pattern 011100101110, which bit is error?
    Groups protected by p1 and p4 are even parity
    But, groups protected by p2 and p8 are odd parity  2 + 8 = 10 and the 10th bit is in error and can be corrected
How to tell if 1- or 2-bit error?
Notes: If 1-bit error for sure, we can correct it. But, if it is possible to be 2-bit error, …?

## Slide 32: Single Error Correcting (SEC) Code
Example 2:
  Consider the code word = 011100101010
  If we detect bit pattern 011100001010, which bit is error?
    Bits 1, 3, 5, 7, 9, 11 should be even parity, but they are not 0 1 1 1 0 0 0 0 1 0 1 0  H = h1h2h4h8 = 1 _ _ _
    Bits 2, 3, 6, 7, 10, 11 should be even parity, but they are not 0 1 1 1 0 0 0 0 1 0 1 0  H = h1h2h4h8 = 1 1 _ _
    Bits 4, 5, 6, 7, 12 should be even parity, but they are not 0 1 1 1 0 0 0 0 1 0 1 0  H = h1h2h4h8 = 1 1 1 _
    Bits 8, 9, 10, 11, 12 should be even parity, and they are 0 1 1 1 0 0 0 0 1 0 1 0  H = h1h2h4h8 = 1 1 1 0
    1 + 2 + 4 = 7 and the 7th bit is in error and can be corrected
Example 3:
  How about this bit pattern: 011100111010?
Notes: If 1-bit error for sure, we can correct it. But, if it is possible to be 2-bit error, …?

## Slide 33: SECDED
Single error correcting, double error detecting (SECDED)
Add an additional parity bit for the whole word (pn)
  Final code word = 011100101010 0
  This makes Hamming distance = 4 (so?)
Decoding: let H = h1h2h4h8 and h n = parity of whole word
  H = 0, hn even  no error
  H  0, hn odd  correctable single bit error (as in SEC)
  H = 0, hn odd  error in pn bit
  H  0, hn even  double error occurred
Note: ECC DRAM uses SECDEC with 8 bits to protect each 64-bit data in memory

## Slide 34: SECDED
Example 1: detect bit pattern = 011100001010 0
  We have shown that H = h1h2h4h8 = 1 1 1 0
  In addition, the whole word is odd parity  hn = odd
  So, H  0, pn odd  correctable single bit error at bit 7
Example 2: detect bit pattern = 011100011010 0
  0 1 1 1 0 0 0 1 1 0 1 0  H = h1h2h4h8 = 1 _ _ _
  0 1 1 1 0 0 0 1 1 0 1 0  H = h1h2h4h8 = 1 1 _ _
  0 1 1 1 0 0 0 1 1 0 1 0  H = h1h2h4h8 = 1 1 1 _
  0 1 1 1 0 0 0 1 1 0 1 0  H = h1h2h4h8 = 1 1 1 1
  The whole word is even parity  hn = even
  So, H  0, hn even  double error