## Slide 1: CS5100 Advanced Computer Architecture Hardware-Based Speculation
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Slides are from textbook, Prof. Hsien-Hsin Lee, Prof. Yasun Hsu)

## Slide 2: About This Lecture
Goal:
  To understand the issues remained unsolved by Tomasulo Algorithm
  To understand the concepts and techniques of hardware-based speculation
Outline:
  Hardware-based speculation (Sec. 3.6)
1

## Slide 3: OOO Commit in Tomasulo Algorithm
In-order issue, but OOO execution, completion, commitment

## Slide 4: What’s Wrong with OOO Commitment?
OOO commit across branch  speculative execution
  Problem: program state is updated speculatively even before the dependent control statement is known to take
What if BNEZ after 1st SD is evaluated to not-taken at cycle 17?
 but 2nd MULTD has updated program state (F4) at cycle 16!

## Slide 5: What’s Wrong with OOO Commitment?
OOO commit under interrupt and resume
  Suppose 1st SD causes a page fault at cycle 17
  An interrupt is raised and hardware saves its PC
  When return from interrupt, execution starts from SD (PC points to it) and all following instructions (LD, MULTD, SD)
  LD and MULTD will be executed again and MULTD will use wrong value in F4  imprecise interrupt
F4
F4

## Slide 6: Desired Features
Want speculative OOO execution beyond branches, but without any consequence
  Speculation: execute an instruction before knowing it should be executed, e.g., beyond a branch
  Without consequences: speculative instructions (if wrongly speculated) must not alter the program states
Want OOO execution with precise interrupt
  All instructions before the interrupted instruction must be completed and committed
  The program state should appear as if no instruction issued after the interrupted instruction
  Maintain “program state” as in sequential execution  restart from saved PC with saved program state

## Slide 7: Hardware-Based Speculation
Basic idea:
  Execute instructions along predicted execution paths but only commit the results if prediction is correct
  Allow OOO execution but commit in-order
Combine three ideas:
  Dynamic OOO instruction scheduling (Tomasulo Algo.)
  Dynamic branch prediction
  Speculative execution: execute instructions before all control dependencies are resolved
Extra hardware requirement:
  Temporary storage to buffer speculative execution result until commit  reorder buffer (ROB)

## Slide 8: Tomasulo Algorithm with Speculation
Key idea: add a commit phase
  Issue
  Execute
  Write result: write results to CDB and store results in a hardware buffer (reorder buffer)
  Commit: update register file or memory if no longer speculative

## Slide 9: Reorder Buffer (ROB)
HW buffer for results of uncommitted instructions
  At least 3 fields: instruction, destination, value
  Can be operand source  virtual registers
  Use reorder buffer # instead of reservation station # as tag ID on CDB
  Supplies operands between execution complete and commit
  After instruction commits, result is put into register
  Easy to undo speculated instr. on mispredicted branches or exceptions
Reorder
Buffer
FP Regs
FP
Op
Queue
FP Adder
FP Adder
Res Stations
Res Stations

## Slide 10: Speculative Tomasulo Algorithm
Issue (IS): get instruction from FP op queue
  If RS and ROB slot free, issue instruction and send operands and ROB no. for destination
  Operands may come from register file or ROB (if not committed yet)
Execution (EX): operate on operands
  When either operands not ready, watch CDB for result (check RAW)
  When both operands in RS, execute

## Slide 11: Speculative Tomasulo Algorithm
Write result (WB): execution complete
  Write on CDB to all awaiting RSs and ROB
Commit: update registers from reorder buffer
  When instruction at head of ROB and result present, update register with result (or store to memory)  change program state
  Remove instruction from ROB
  Mispredicted branch flushes ROB

## Slide 12: Commit Step
New step for making instruction execution “visible” to the outside world, e.g., assembly program
  It “commits” the changes to the program state
A
B
C
D
E
F
G
H
J
K










ARF
commit
Outside World “sees”:
A executed
B executed
C executed
D executed
E executed
ROB
Instructions executed out of program order,
but outside world still “believes” it is in-order
ROB head
tail
Architecture register file
Notes: From GIT’s Loh.

## Slide 13: Handling Incorrect Speculation
Instructions following mispredicted branch, i.e. those in decode/issue buffers & RSs, are flushed
ROB entries of these instructions are deallocated
Restart fetch at correct branch successor
Kill
update
Kill
Kill
Branch
Resolution
Inject correct PC
Branch
Prediction
Fetch
Decode
Execute
Commit
Reorder Buffer
PC
Complete

## Slide 14: Handling Precise Exception/Interrupt
Must ensure exceptions/interrupts in program order for precise interrupt
Idea: take care of exceptions at commit time
  If an instruction raises exception, wait until it reaches head of ROB and then takes interrupt, flushes any other pending instructions
  Instructions behind it are re-executed
  Because instructions commit in order, this yields a precise exception

## Slide 15: Handling Precise Exception/Interrupt
Instructions fetched and decoded into ROB in-order
Execution is out-of-order  OOO completion
Commit (write-back to program state, i.e., register file and memory) is in-order
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order
In-order
Out-of-order
Exception?
Kill
Kill
Kill
Inject handler PC

## Slide 16: Tomasulo without Speculation
Addr
Data addr

## Slide 17: Tomasulo with Speculation via ROB
Load addr

## Slide 18: Speculative Tomasulo with ROB
FP adders
FP multipliers
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
LD F0,10(R2)
N
Done?
Dest
Dest
Oldest
Newest
ROB1 10+R2
Dest
Reorder Buffer
Registers
value instn
dest
To Memory
From Memory
For load
For store
Stall
Notes: LD encounters a cache miss

## Slide 19: Speculative Tomasulo with ROB
ROB2 ADDD R(F4),LD1
FP adders
FP multipliers
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F10
F0
ADDD F10,F4,F0
LD F0,10(R2)
N
N
Done?
Dest
Dest
Oldest
Newest
ROB1 10+R2
Dest
Reorder Buffer
Registers
value instn
dest
To Memory
From Memory
For load
For store

## Slide 20: Speculative Tomasulo with ROB
ROB3 DIVD ADD1,R(F6)
ROB2 ADDD R(F4),LD1
FP adders
FP multipliers
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Oldest
Newest
ROB1 10+R2
Dest
For load
For store
To Memory
From Memory
Registers
Dest
Dest
Done?
value instn
dest
Reorder Buffer

## Slide 21: Speculative Tomasulo with ROB
ROB3 DIVD ADD1,R(F6)
ROB2 ADDD R(F4),LD1
ROB6 ADDD LD2, R(F6)
FP adders
FP multipliers
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
ADDD F0,F4,F6
N
F4
LD F4,0(R3)
N
--
BNE F0,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Oldest
Newest
ROB1 10+R2
Dest
ROB5 0+R3
To Memory
From Memory
Dest
Dest
Registers
Done?
value instn
dest
Reorder Buffer
For load
For store
Notes: WAW hazard on F0

## Slide 22: Speculative Tomasulo with ROB
ROB3 DIVD ADD1,R(F6)
ROB2 ADDD R(F4),LD1
ROB6 ADDD LD2, R(F6)
FP adders
FP multipliers
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
ST 0(R3),F4
ADDD F0,F4,F6
N
N
F4
LD F4,0(R3)
N
--
BNE F0,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Oldest
Newest
Dest
ROB1 10+R2
ROB5 0+R3
To Memory
From Memory
Dest
Dest
Registers
Done?
value instn
dest
Reorder Buffer
For load
For store

## Slide 23: Speculative Tomasulo with ROB
ROB3 DIVD ADD1,R(F6)
FP adders
FP multipliers
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
ST 0(R3),F4
ADDD F0,F4,F6
N
N
F4
M[10]
LD F4,0(R3)
Y
--
BNE F0,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Oldest
Newest
ROB1 10+R2
Dest
ROB2 ADDD R(F4),LD1
ROB6 ADDD M[10],R(F6)
For load
For store
To Memory
From Memory
Dest
Dest
Registers
Done?
value instn
dest
Reorder Buffer
Notes: 2nd LD completed
RS2 of adder is ready

## Slide 24: Speculative Tomasulo with ROB
ROB3 DIVD ADD1,R(F6)
ROB2 ADDD R(F4),M[50]
FP adders
FP multipliers
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
ST 0(R3),F4
ADDD F0,F4,F6
N
Ex
F4
M[10]
LD F4,0(R3)
Y
--
BNE F0,<…>
N
F2
F10
F0
M[50]
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
Y
Oldest
Newest
Dest
For load
For store
To Memory
From Memory
Dest
Dest
Registers
Done?
value instn
dest
Reorder Buffer
Notes: 2nd ADDD fired into FP adder
RS1 for 1st ADDD is ready
1st LD completed

## Slide 25: Speculative Tomasulo with ROB
ROB3 DIVD ADD1,R(F6)
FP adders
FP multipliers
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
N
Y
F4
M[10]
LD F4,0(R3)
Y
--
BNE F0,<…>
N
F2
F10
DIVD F2,F10,F6
ADDD F10,F4,F0
N
Ex
Oldest
Newest
Dest
For load
For store
To Memory
From Memory
Dest
Dest
Registers
M[50]
Done?
value instn
dest
Reorder Buffer
F0
Program state changed
Notes: 1st LD commit to register F0
2nd ADDD completed
1st ADDD fired

## Slide 26: Speculative Tomasulo with ROB
ROB3 DIVD <val1>,R(F6)
FP adders
FP multipliers
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
N
Y
F4
M[10]
LD F4,0(R3)
Y
--
BNE F0,<…>
N
F2
F10
<val1>
DIVD F2,F10,F6
ADDD F10,F4,F0
N
Y
Oldest
Newest
Dest
For load
For store
To Memory
From Memory
Dest
Dest
Registers
M[50]
Done?
value instn
dest
Reorder Buffer
F0
BNE mispredicted
Notes: 1st ADDD completed
BNE found to be mispredicted

## Slide 27: Speculative Tomasulo with ROB
ROB3 DIVD <val1>,R(F6)
FP adders
FP multipliers
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
BNE F0,<…>
Y
F2
F10
<val1>
DIVD F2,F10,F6
ADDD F10,F4,F0
N
Y
Oldest
Newest
Dest
For load
For store
To Memory
From Memory
Dest
Dest
Registers
M[50]
Done?
value instn
dest
Reorder Buffer
F0
All speculative instructions are flushed!

## Slide 28: Speculative Tomasulo with ROB
ROB5 ADDD R(F6),MULT1
FP adders
FP multipliers
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F5
ADDD F5,F6,F2
N
--
BNE F0,<…>
Y
F2
DIVD F2,F10,F6
Ex
Oldest
Newest
Dest
For load
For store
To Memory
From Memory
Dest
Dest
Registers
M[50]
Done?
value instn
dest
Reorder Buffer
F0
F[10]  <val1>
New instructions fetched from correct path
Notes: 1st ADDD committed and register F10 is updated
1st DIVD fired
New instructions fetched from correct path

## Slide 29: ROB Handling Precise Interrupts
Head
Tail
V
Data (physical register)
Exp
event
RegDst
Done?
Spec?
PC
.
.
.
.
.
.
1
0
0
xA000
0000
R1
1
0
0
xA004
0000
R2
R1=R1+10
R2=R2*2
1
0
0
xA008
0000
FR1
FR1=FR2/0.0
1
0
11
1
R1
11
1
R2
1
ARF
R31
1
1
R3
R4
2
3
4

## Slide 30: ROB Handling Precise Interrupts
Head
V
Data (physical register)
Exp
event
RegDst
Done?
Spec?
PC
.
.
.
.
.
.
0
1
0
0
xA004
0000
R2
R2=R2*2
1
0
0
xA008
0000
FR1
FR1=FR2/0.0
Tail
1
0
0
xA00C
0000
R3
R3=R3+1
1
R1
11
1
R2
1
ARF
R31
1
1
R3
R4
2
3
4

## Slide 31: ROB Handling Precise Interrupts
Head
V
Data (physical register)
Exp
event
RegDst
Done?
Spec?
PC
.
.
.
.
.
.
0
1
0
0
xA004
0000
R2
R2=R2*2
1
0
0
xA008
0000
FR1
FR1=FR2/0.0
Tail
1
0
1
xA00C
0000
R3
R3=R3+1
1
0
0
xA010
0000
R4
4
R4=R4*2
1
R1
11
1
R2
1
ARF
R31
1
1
R3
R4
2
3
4

## Slide 32: ROB Handling Precise Interrupts
Head
V
Data (physical register)
Exp
event
RegDst
Done?
Spec?
PC
.
.
.
.
.
.
0
1
0
0
xA004
0000
R2
R2=R2*2
1
0
0
xA008
0000
FR1
FR1=FR2/0.0
Tail
1
0
1
xA00C
0000
R3
R3=R3+1
1
0
1
xA010
0000
R4
4
R4=R4*2
8
1
0
0
xA014
0000
FR4
LD FR4,M[50]
1
4
1
R1
11
1
R2
1
ARF
R31
1
1
R3
R4
2
3
4
4
0101
Exception raised

## Slide 33: ROB Handling Precise Interrupts
V
Data (physical register)
Exp
event
RegDst
Done?
Spec?
PC
.
.
.
.
.
.
0
1
0
0
xA008
0000
FR1
FR1=FR2/0.0
Tail
1
0
1
xA00C
0000
R3
R3=R3+1
1
0
1
xA010
0000
R4
4
R4=R4*2
8
1
0
0
xA014
0101
FR4
1
0
1
xA004
0000
R2
R2=R2*2
4
0
Head
1
R1
11
1
R2
1
ARF
R31
1
1
R3
R4
4
3
4
LD FR4,M[50]
Exception raised
0010

## Slide 34: ROB Handling Precise Interrupts
V
Data (physical register)
Exp
event
RegDst
Done?
Spec?
PC
.
.
.
.
.
.
0
1
0
0
xA008
0010
FR1
FR1=FR2/0.0
Tail
1
0
1
xA00C
0000
R3
R3=R3+1
1
0
1
xA010
0000
R4
4
R4=R4*2
8
1
0
0
xA014
0101
FR4
Head
0
These values were not committed into RF but flushed
Depending on the exception, process will either abort or instructions will be resumed from this faulting instruction
1
R1
11
1
R2
1
ARF
R31
1
1
R3
R4
4
3
4
LD FR4,M[50]
Push “PC” and current RF into stack
Exception detected

## Slide 35: ROB Handling Precise Interrupts
V
Data (physical register)
Exp
event
RegDst
Done?
Spec?
PC
.
.
.
.
.
.
0
1
0
0
xA008
0000
FR1
FR1=FR2/0.0
Tail
1
0
0
xA00C
0000
R3
R3=R3+1
1
0
0
xA010
0000
R4
R4=R4*2
1
0
0
xA014
0000
FR4
Head
0
1
R1
11
1
R2
1
ARF
R31
1
1
R3
R4
4
3
4
LD FR4,M[50]
After exception, “PC” and RF are popped back and all following instructions are executed again

## Slide 36: Recap
Problems with dynamic scheduling
  OOO commit on speculative execution
  OOO commit on precise interrupt
Hardware-based speculation
  Execute instructions before knowing whether they should be executed
  OOO execution and completion, in-order commit through ROB, dynamic scheduling, branch prediction
  Solve both precise interrupt and speculative execution at the same time

## Slide 37: Program State: Basic Idea
Suppose initially i = 0 and x = 0.5
code program state
...
  i = i+1;
  x = 1.5
  ...
Machine code can be viewed similarly
  1000 ld R1,0(Ri)
  1004 add R1,R1,#1
  1008 sd R1,0(Ri)
  1016 ld F2,0(Rx)
  ...
… i=0 x=0.5 ...
… i=1 x=0.5 ...
… i=1 x=1.5 ...
S1
S2
S3
Finite-state machine
Program state includes registers and control registers, e.g. PC and status reg.
i=i+1
x=1.5
Program can be interrupted and resumed as long as state is preserved