## Slide 1: CS4100: Computer Architecture Course Overview
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Adapted from textbook slides https://www.elsevier.com/books-and-journals/book-companion/9780128122754/lecture-slides)

## Slide 2: Computers Are Pervasive
You find computers everywhere
We cannot live our daily life without them

## Slide 3: Surprisingly, Computers Are Similar Inside
Processor
(active)
Computer
Control
(“brain”)
Datapath
(“process”)
Memory
(passive)
(where
programs,
data live when
running)
Devices
Input
Output
Keyboard, Mouse
Display, Speaker
Disk (where programs, data live when not running), Network
Interconnection
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1. The input devices bring the data from the outside world into the computer.
2. These data are kept in the computer’s memory until ...
3. The datapath request and process them.
4. The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world.
5. Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 4: Outline
Why this course?
  How does a computer work?
  And, where does computer architecture stand?
Course outline
Course administration

## Slide 5: Let Us Start with a Program
We develop programs in high-level languages (HLL) through an integrated development environment (IDE)
  HLL provides a level of abstraction closer to problem domain that is good for productivity and portability
  Programs implement algorithms and often take input data, process them, produce output data
swap(int v[], int k) {
int temp;
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}

## Slide 6: Program Translated to Machine Code
The HLL program must be translated into machine instructions to instruct computer processor how to execute (e.g. process input to produce output)
A compiler (called by IDE) translates a HLL program into an assembly language program
  Textual representation of machine instructions
Compiler

## Slide 7: Program Translated to Machine Code
An assembler translates an assembly language program into machine executable code
An linker links separately compiled code modules and shared libraries into an executable program (file) containing encoded machine instructions and data, whereas the file is stored on the disk
Assembler

## Slide 8: When the Program Is to Be Executed
Operating system uses a loader to load (part of) the binary executable program from disk into memory and prepare the executable code for running
Once loading is completed, operating system starts the program by passing CPU control to the loaded program code
Now computer hardware part starts to work to execute this program
Processor
Control
Datapath
Memory
Devices
Interconnection
001101001011
001101001011

## Slide 9: Processor Executes the Machine Code
The computer processor fetches instructions from the program code in the memory and processes data in the memory as instructed
Z
N
Register
Memory
PC
IR
Controller
ALU
clock
Control signals
Datapath
Control
001101001011
001101001011
0011
0100
0111
+

## Slide 10: Inside the Processor
Components (registers, ALU) consist of logic gates via logic design
http://gyan.fragnel.ac.in/~surve/COA/ISA/FixedPoint.html
http://users.ece.utexas.edu/~valvano/Volume1/E-Book/C4_DigitalLogic_files/image014.gif
register
adder

## Slide 11: Logic Gate Can Be Made by Transistors
CMOS NAND:
Transistors are nothing but ON/OFF switches

## Slide 12: A Transistor to Switch ON/OFF
ON
OFF
This is a topic of electronic and circuit design

## Slide 13: Where Computer Architecture Stand?
Computer architecture is not just computer hardware
Instruction Set Architecture (ISA)
Processor
Operating System
Application
Digital Design
Circuit Design
Datapath & Control
Transistors
Hardware
Software
Compiler
Assembler
Memory
I/O System

## Slide 14: Instruction Set Architecture (ISA)
Instruction Set Architecture (or architecture in short)
  An abstract interface between the hardware and the lowest-level software
  Encompasses all the information necessary to write a machine language program that will run correctly, including instructions, registers, memory access, I/O, and so on
Why ISA important?
  Enables many implementations of that architecture of varying cost and performance to run identical software, e.g. different x86 processors to run same Windows OS
  Allows computer designers to design functions independently from the hardware that implements them

## Slide 15: Example ISA
Intel 8051 (8-bit microcontroller) 1980-
TI MSP-430 (16-bit microcontroller) 1993-
Digital Alpha (v1, v3) 1992-2004
HP PA-RISC (v1.1, v2.0) 1986-2008
Sun Sparc (v8, v9) 1987-2017
MIPS (I ~ V, 32/64) 1985-
Intel x86 (8086,80286,80386, 1978- 80486,Pentium, MMX, SIMD, IA-64, ...)
ARM (v2~v7, v8) 1985-
RISC-V (v2.2) 2010-

## Slide 16: Computer Architecture Is Thus about …
SW/HW interface (ISA)
Computer organization
Quantitative design methodology (based on performance, power, cost, …)
ISA

## Slide 17: Outline
Why this course?
  How does a computer work?
  And, where does computer architecture stand?
Course outline
Course administration

## Slide 18: What You Will Learn
How programs are translated into the machine language
  And how the hardware executes them
The hardware/software interface
What determines program performance
  And how it can be improved
How computer hardware (processor, memory) works
How hardware designers improve performance
What is parallel processing

## Slide 19: Textbook
Computer Organization and Design RISC-V Edition: The Hardware/Software Interface, 1st ed., David Patterson and John Hennessy, Morgan Kaufmann, Apr. 2017

## Slide 20: Topics Covered
Topic Chapter
Computer Abstractions and Technology 1
Instructions: Language of the Computer 2
Arithmetic for Computers 3
The RISC-V Processor 4
Large and Fast: Exploiting Memory Hierarchy 5
Parallel Processors from Client to Cloud 6

## Slide 21: Outline
Why this course?
  How does a computer work?
  And, where does computer architecture stand?
Course outline
Course administration

## Slide 22: Course Administration: CS4100-01
授課老師: 金仲達
  辦公室: 台達640
  電話: 42804
  email: king@cs.nthu.edu.tw
上課時間:
  星期二10:10-12:00
  星期四10:10-11:00
上課地點: 台達館105室
課程網頁:
  iLSM
  http://www.cs.nthu.edu.tw/~king/courses/cs4100.html

## Slide 23: Prerequisites
Programming:
  Any programming language (C or C++ preferred)
Logic design:
  Logic equations, schematic diagrams, finite state machine

## Slide 24: Expected Course Workload
Learn processor emulators and benchmarking
4~7 homework assignments
  Assignments are a mixture of design, calculation, programming, measurement, and discussion problems
  Assignments will be posted on iLMS
  Independent of, but complement, examinations
One mid-term and one final examination
Grade breakdown (may adjust final grades)
  Homework assignments 50%
  Class participation and quiz 10%
  Midterm exam 20%
  Final exam 20%
Can bring 1-page note of A4 size

## Slide 25: Resources on the Internet
Course website of Prof. Tingting Hwang
  http://www.cs.nthu.edu.tw/~tingting/cs4100.html
Open Course Ware (OCW)
  http://ocw.nthu.edu.tw/ocw/index.php?page=course&cid=76&
ShareCourse
  http://www.sharecourse.net/sharecourse/course/view/courseInfo/26
MOOCs
  http://mooc.nthu.edu.tw/sharecourse/course/view/courseInfo/112 <-- need to register for the course first
Online resources of textbook:
  https://www.elsevier.com/books-and-journals/book-companion/9780128122754

## Slide 26: Course Problems
Cannot turn in homework on time
  No late homework is accepted
Forgot to turn in homework/Dog ate computer
  ???
What is cheating?
  Study together in groups is encouraged
  Work must be your own

## Slide 27: Course Schedule
No class on the following days:
  3/26 (Tue.): 2 hr
  3/28 (Thu.): 1 hr
  4/18 (Thu.): 1 hr
Makeup plan: class on selected Thursdays 11:00-12:00
  3/7
  3/14
  3/21
  4/11