## Slide 1: CS4100: Computer Architecture Arithmetic for Computers
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Adapted from textbook slides https://www.elsevier.com/books-and-journals/book-companion/9780128122754/lecture-slides)

## Slide 2: Outline
Addition and subtraction (Sec. 3.2)
  Constructing a basic ALU (Sec. A.5)
Multiplication (Sec. 3.3)
Division (Sec. 3.4)
Floating point (Sec. 3.5)
Parallelism and computer arithmetic: subword parallelism (Sec. 3.6)
Streaming SIMD extensions and advanced vector extensions in x86 (Sec. 3.7)
Subword parallelism and matrix multiply (Sec. 3.8)

## Slide 3: Constructing a Basic ALU
Support the following arithmetic and logic operations
  add, sub: two’s complement addition/subtraction with overflow detection
  and, or, nor: bitwise logical AND, logical OR, logical NOR
  slt (set-on-less-than): compare two input numbers (by subtraction) and output a 1 if first is less than second, otherwise output a 0
Register
ALU
To controller
CPU
Datapath
From controller
ALUop
V
Z
Notes: Let’s design an Arithmetic Logic Unit for the RISC-V CPU that can perform bitwise AND, bitwise OR, binary add, binary subtract, and set-on-less-than.

## Slide 4: Functional Specification
ALU
64
64
64
A
B
Result
Overflow
Zero
4
ALUop
CarryOut
Fig. A.5.13
Fig. A.5.14
ALU Control (ALUop) | Function
0000 | and
0001 | or
0010 | add
0110 | sub
0111 | set-less-than
1100 | nor
Notes: The type of operation the ALU perform will be selected by the ALUop bits.
The ALU I am going to show you in class is 4 bits wide (N = 4). The ALU in RISC-V will be 64 bits wide.

## Slide 5: Design Strategy: Bit-slice ALU
Design trick: divide and conquer
  Break the problem into simpler problems, solve individual problems and glue together the solutions
ALU63
a63
b63
m
cin
c63
s63
A
B
ALUop
Result
64
64
64
4
Overflow
ALU0
a0
b0
m
cin
c0
s0
Zero

## Slide 6: Zoom-in to 1-bit ALU
Fig. A.5.6
A
B
1-bit
Full
Adder
CarryOut
Mux
CarryIn
Result
add
and
or
Operation
0
1
2
2
ALU Control (ALUop) | Function
0000 | and
0001 | or
0010 | add
0110 | sub
0111 | set-on-less
1100 | nor
All logic gates operate to produce results and only the desired one is chosen
Only combinational logic
Notes: Now that I have shown you how to build a 1-bit full adder, we have all the major components needed for this 1-bit ALU.
In order to build a 4-bit ALU, we simply connect four 1-bit ALUs in series to feed the CarryOut of one ALU to the CarryIn of the next ALU.
Even though I called this an ALU, I actually lied a little. There is something missing about this ALU. This ALU can NOT perform the subtract operation.
Let see how can we fix this problem.
2 min = 35 min. (Y:15)

## Slide 7: Recall 1-Bit Full Adder
Fig. A.5.3
https://commons.wikimedia.org/wiki/File:Full-adder.svg

## Slide 8: From 1-bit to 4-bit ALU
1-bit ALU 4-bit ALU
A0
B0
1-bit
ALU
Result0
CarryIn0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
CarryOut2
A3
B3
1-bit
ALU
Result3
CarryIn3
CarryOut3
Operation
A_i
B_i
1-bit
Full
Adder
CarryOut_i
Mux
CarryIn_i
Result
Operation
2
2
Ripple-carry adder
Notes: Now that I have shown you how to build a 1-bit full adder, we have all the major components needed for this 1-bit ALU.
In order to build a 4-bit ALU, we simply connect four 1-bit ALUs in series to feed the CarryOut of one ALU to the CarryIn of the next ALU.
Even though I called this an ALU, I actually lied a little. There is something missing about this ALU. This ALU can NOT perform the subtract operation.
Let see how can we fix this problem.
2 min = 35 min. (Y:15)

## Slide 9: How about Subtraction?
ALU
A
B’
Result
CarryIn
CarryOut
B
0
1
Mux
Sel
Subtract
(Bnegate)
2’s complement operation: take inverse of every bit and add 1 (at cin of first stage)
So, subtraction becomes addition of 2’s complement
  A – B = A + (-B) = A + (B’ + 1) = A + B’ + 1
  B’: bit-wise inverse of B
Fig. A.5.8
Operation
2
1
Notes: Recalled something you learned from grade school that: A - B is the same as A plus (-B).
Also recall from earlier slides that in order to calculate the 2’s complement representation of negative B, we simply take the inverse of very bit and add 1.
The bitwise inverse of B is easy to compute. Just pass them through the inverter.
In order to do the add 1 operation, we simply set the CarryIn to 1.
So for the subtract operation, we simply select the output of the inverter and set CarryIn to 1.
Then we will be adding A to the negative of B and whola, we have the A minus B operation.
+2 = 37 min. (Y:17)

## Slide 10: Zoom-in to 1-bit ALU
A
B
1-bit
Full
Adder
CarryOut
Mux
CarryIn
Result
add
and
or
Operation
0
1
2
2
Fig. A.5.8
ALUop | Function
0000 | and
0001 | or
0010 | add
0110 | sub
0111 | set-on-less
1100 | nor
B’
B
0
1
Mux
Sel
Subtract
(Bnegate)

## Slide 11: Revised Diagram
LSB and MSB need to do a little extra
A
B
ALUop
Result
64
64
64
4
Overflow
ALU0
a0
b0
cin
c0
s0
ALU63
a63
b63
cin
c63
s63
Supply a 1 on subtraction
?
Zero
Combining the CarryIn and Bnegate

## Slide 12: Zoom-in to Rightmost Bit of ALU
A
B
1-bit
Full
Adder
CarryOut
Mux
CarryIn
Result
add
and
or
Operation
0
1
2
2
Fig. A.5.8
B’
B
0
1
Mux
Sel
Bnegate
ALUop | Function
0000 | and
0001 | or
0010 | add
0110 | sub
0111 | set-on-less
1100 | nor

## Slide 13: Overflow of Signed Integer Addition
Decimal Binary Decimal 2’s complement
0 0000 0 0000
1 0001 -1 1111
2 0010 -2 1110
3 0011 -3 1101
4 0100 -4 1100
5 0101 -5 1011
6 0110 -6 1010
7 0111 -7 1001
-8 1000
Ex: 7 + 3 = 10 but ... - 4 - 5 = - 9 but …
0 1 1 1 1 0 0 0
0 1 1 1 7 1 1 0 0 -4
+ 0 0 1 1 3 + 1 0 1 1 -5
1 0 1 0 -6 0 1 1 1 7
S
S

## Slide 14: Overflow Detection
Overflow: result too big/small to represent
  -8  4-bit binary number  7
  Adding operands with different signs  no overflow
  Overflow occurs when adding:
    2 positive numbers and the sum is negative
    2 negative numbers and the sum is positive
     sign bit is set with the value of the result
  Overflow: if Carry into MSB  Carry out of MSB
0 1 1 1 1 0 0 0
0 1 1 1 7 1 1 0 0 -4
+ 0 0 1 1 3 + 1 0 1 1 -5
1 0 1 0 -6 0 1 1 1 7
Notes: Recalled from some earlier slides that the biggest positive number you can represent using 4-bit is 7 and the smallest negative you can represent is negative 8.
So any time your addition results in a number bigger than 7 or less than negative 8, you have an overflow.
Keep in mind is that whenever you try to add two numbers together that have different signs, that is adding a negative number to a positive number, overflow can NOT occur.
Overflow occurs when you to add two positive numbers together and the sum has a negative sign. Or, when you try to add negative numbers together and the sum has a positive sign.
If you spend some time, you can convince yourself that If the Carry into the most significant bit is NOT the same as the Carry coming out of the MSB, you have a overflow.
+2 = 41 min. (Y:21)

## Slide 15: Overflow Detection Logic
A0
B0
1-bit
ALU
Result0
CarryIn0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
A3
B3
1-bit
ALU
Result3
CarryIn3
CarryOut3
Overflow
X
Y
X XOR Y
0
0
0
0
1
1
1
0
1
1
1
0
Overflow = CarryIn[N-1] XOR CarryOut[N-1]
Notes: Recall the XOR gate implements the not equal function: that is, its output is 1 only if the inputs have different values.
Therefore all we need to do is connect the carry into the most significant bit and the carry out of the most significant bit to the XOR gate.
Then the output of the XOR gate will give us the Overflow signal.
+1 = 42 min. (Y:22)

## Slide 16: Nor Operation
A nor B = (not A) and (not B)
0
Operation
1
0
1
b
2
Fig. A.5.9
ALUop
Result
CarryOut
Ainvert
CarryIn
0
1
a
Bnegate
2
ALUop Function
0000 and
0001 or
0010 add
0110 subtract
0111 set-less-than
1100 nor
operation
Bnegate
Ainvert
Z
V
Register
PC
IR
Controller
ALU
clock
Control signals
Datapath
Control

## Slide 17: Zero Detection Logic
CarryIn0
A0
B0
1-bit
ALU
Result0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
CarryOut2
A3
B3
1-bit
ALU
Result3
CarryIn3
CarryOut3
Zero
To support conditional jump: by a one BIG NOR gate
Notes: Besides detecting overflow, our ALU also needs to indicate if the result is zero.
This is easy to do. All we need is a BIG NOR gate.
Then if any of the Result bit is not zero, then the output of the NOR gate will be low.
The only time the output of the NOR gate is high is when all the result bits are zeroes.
+1 = 43 min. (Y:23)

## Slide 18: Set-on-Less-Than
If A < B, then Result = 00..01, else Result = 00..00
If (A – B) < 0, then Result = 00..01, else Result = 00..00
If A – B & sign of Result is 1, then Result = 00..01, else Result = 00..00
If A – B & Result63 = 1, then Result = 00..01, else Result = 00..00
If A – B & Result63 = 1, then Result0 = 1, else Result0 = 0, while Result63 ~ Result1 = 0
A – B & Result0 = Result63, while Result63 ~ Result1 = 0
  No need to do if-then-else test

## Slide 19: Set on Less Than (I)
1-bit in ALU (for bits 0~62)
0
3
Operation
1
0
1
b
2
Fig. A.5.10a
ALUop
Less
Result
CarryOut
Ainvert
CarryIn
0
1
a
Bnegate
2
ALUop Function
0000 and
0001 or
0010 add
0110 subtract
0111 set-less-than
1100 nor
operation
Bnegate
Ainvert
Still perform a subtraction
Copy input to output
But choose input as output

## Slide 20: Set on Less than (II)
Sign bit in ALU (bit 63)
Overflow
detection
0
3
Operation
a
1
0
1
b
2
Fig. A.5.10b
Less
Result
Ainvert
CarryIn
Set
Overflow
Bnegate
0
1
2
If A-B < 0, Set =1

## Slide 21: Final 64-Bit ALU
ALUop Function
0000 and
0001 or
0010 add
0110 subtract
0111 set-less-than
1100 nor
Fig. A.5.12
Z
V
Register
PC
IR
Controller
ALU
clock
Control signals
Datapath
Control
63
63
63
63

## Slide 22: Verilog Behavioral Definition of 64-Bit ALU
module RISCVALU(ALUctl, A, B, ALUOut, Zero);
input [3:0] ALUctl;
input [63:0] A,B;
output reg [63:0] ALUOut;
output Zero;
assign Zero = (ALUOut==0); //Zero true if ALUOut 0
always @(ALUctl, A, B) begin //reevaluate if change
case (ALUctl)
0: ALUOut <= A & B;
1: ALUOut <= A | B;
2: ALUOut <= A + B;
6: ALUOut <= A - B;
7: ALUOut (= A < B ? 1 : 0;
12: ALUOut <= ~(A | B); // nor
default: ALUOut <= 0;
endcase
end
endmodule
Fig. A.5.15
ALUop Function
0000 and
0001 or
0010 add
0110 subtract
0111 set-less-than
1100 nor

## Slide 23: RISC-V ALU Control
module ALUControl (ALUOP, FuncCode, ALUCtl);
input [1:0] ALUOP;
input [5:0] FuncCode;
output [3:0] reg ALUCtl;
always case (FuncCode)
32: ALUOP <= 2; // add
34: ALUOP <= 6; // subtract
36: ALUOP <= 0; // and
37: ALUOP <= 1; // or
39: ALUOP <= 12; // nor
42: ALUOP <= 7; // slt
default: ALUOP <= 15; // should not happen
endcase
endmodule
Fig. A.5.16

## Slide 24: Problems with Ripple Carry Adder
Carry bit may have to propagate from LSB to MSB  worst case delay: N-stage delay
A0
B0
1-bit
ALU
Result0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
A3
B3
1-bit
ALU
Result3
CarryIn3
CarryOut3
CarryOut2
CarryIn0
CarryIn
CarryOut
A
B
By Marble machine - Own work, CC BY-SA 4.0,
https://commons.wikimedia.org/w/index.php?curid=48016289
Notes: The Adder we just built is called a Ripple Carry Adder because: Carry may have to propagate from the least significant bit to the most significant bit.
In other words, the combination of A0, B0, and CarryIn0 may cause CarryOut0 to become 1.
As a result of CarryOut0 going 1, CarryOut1 may become 1 and etc., etc., .... etc and propagate down the carry chain.
Recall the Carry Logic: CarryIn to CarryOut has a 2-gate delay.
So in the worst case, a N-bit ripple carry will have a 2N gate delay.
For a 32-bit adder, this means the worst case delay is 64 gates. This can be a problem.
So after the break, I will show you some faster way of designing an ALU.
+2 = 45 min. (Y:25)

## Slide 25: Improving Ripple Carry Adder
Strategy: determine carry in to high-order bits sooner
How? Examine how carry is generated and propagated
  Carry generation: under what condition a carry is generated at a bit stage?
    If a=1 and b=1, a carry is generated no matter what the value of carry input is Generate = g = a & b
  Carry propagation: under what condition a carry can be propagated at a bit stage?
    If only a=1 or only b=1, the value of carry input is propagated to the carry output Propagate = p = a xor b

## Slide 26: Improving Ripple Carry Adder
Carry skip adder:
  Pi-1,k = 0  this stage will not propagate carry  the result of the carry is generated within this stage
http://www.syssec.ethz.ch/education/Digitaltechnik_14
X

## Slide 27: Improving Ripple Carry Adder
Carry lookahead adder:
  Look ahead and anticipate the carry to come (Sec. B.6)
http://www.syssec.ethz.ch/education/Digitaltechnik_14
Fixed delay
Notes: Cout will have a carry if An-1 and Bn-1 can generate a carry, or they can propagate a carry and An-2 and Bn-2 can generate a carry, …

## Slide 28: Improving Ripple Carry Adder
Carry select adder:
  Design principle: parallelism (do both paths first and choose the desired result after carry in is known)
http://www.syssec.ethz.ch/education/Digitaltechnik_14

## Slide 29: Outline
Addition and subtraction (Sec. 3.2)
Multiplication (Sec. 3.3)
Division (Sec. 3.4)
Floating point (Sec. 3.5)
Parallelism and computer arithmetic: subword parallelism (Sec. 3.6)
Streaming SIMD extensions and advanced vector extensions in x86 (Sec. 3.7)
Subword parallelism and matrix multiply (Sec. 3.8)

## Slide 30: Unsigned Multiply
Paper and pencil example (unsigned):
1000 X 1001 00001000 00000000 00000000 01000000 01001000
m bits x n bits = m+n bit product
Binary makes it easy:
  0  place 0 ( 0 x multiplicand)
  1  place a copy ( 1 x multiplicand)
Multiplicand
Multiplier
Product

## Slide 31: Unsigned Multiplier for RISC-V (Ver. 1)
128-bit multiplicand register (with 64-bit multiplicand at right half), 128-bit ALU, 128-bit product register, 64-bit multiplier register
Fig. 3.3

## Slide 32: Multiply Algorithm (Ver. 1)
3. Shift Multiplier register right 1 bit
2. Shift Multiplicand register left 1 bit
0010 x 0011
Product Multiplier Multiplicand
0000 0000 0011 0000 0010
0000 0010 0001 0000 0100
0000 0110 0000 0000 1000
0000 0110 0000 0001 0000
0000 0110 0000 0010 0000
Done
Yes: 64 repetitions
No: < 64 repetitions
1. Test
Multiplier0
Multiplier0 = 0
Multiplier0 = 1
1a. Add multiplicand to product and
place the result in Product register
64th
repetition?
Start
Fig. 3.4
Notes: Mpler: 0011 Mcand: 0000 0010 P: 0000 0000
1a. 1=>P=P+Mcand Mpler: 0011 Mcand: 0000 0010 P: 0000 0010
2. Shl Mcand Mpler: 0011 Mcand: 0000 0100 P: 0000 0010
3. Shr Mpler Mpler: 0001 Mcand: 0000 0100 P: 0000 0010
1a. 1=>P=P+Mcand Mpler: 0001 Mcand: 0000 0100 P: 0000 0110
2. Shl Mcand Mpler: 0001 Mcand: 0000 1000 P: 0000 0110
3. Shr Mpler Mpler: 0000 Mcand: 0000 1000 P: 0000 0110
1. 0=>nop Mpler: 0000 Mcand: 0000 1000 P: 0000 0110
2. Shl Mcand Mpler: 0000 Mcand: 0001 0000 P: 0000 0110
3. Shr Mpler Mpler: 0000 Mcand: 0001 0000 P: 0000 0110
1. 0=>nop Mpler: 0000 Mcand: 0001 0000 P: 0000 0110
2. Shl Mcand Mpler: 0000 Mcand: 0010 0000 P: 0000 0110
3. Shr Mpler Mpler: 0000 Mcand: 0010 0000 P: 0000 0110

## Slide 33: Observations: Multiply Ver. 1
If 1 clock per iteration  64 clocks per multiply
  Ratio of multiply to addition 5:1 to 100:1
Half of the bits in multiplicand always 0  128-bit adder is wasteful
0’s inserted in right of multiplicand as shifted  least significant bits of product never changed once formed
Instead of shifting multiplicand to left, shift product to right?
Product register wastes space  combine Multiplier and Product register

## Slide 34: Unsigned Multiplier for RISC-V (Ver. 2)
64-bit Multiplicand register, 64-bit ALU, 128-bit Product register (0-bit Multiplier register)
Fig. 3.5

## Slide 35: Multiply Algorithm (Ver. 2)
64th
repetition?
2. Shift Product register right 1 bit
1a. Add multiplicand to left half of product and
place the result in left half of Product register
Multiplicand Product 0010 0000 0011
0010 0011
0010 0001 0001
0011 0001
0010 0001 1000
0010 0000 1100
0010 0000 0110
Done
Yes: 64 repetitions
No: < 64 repetitions
1. Test
Product0
Product0 = 0
Product0 = 1
Start
Notes: Mcand: 0010 P: 0000 0011
1a. 1=>P=P+Mcand Mcand: 0010 P: 0010 0011
2. Shr P Mcand: 0010 P: 0001 0001
1a. 1=>P=P+Mcand Mcand: 0010 P: 0011 0001
2. Shr P Mcand: 0010 P: 0001 1000
1. 0=>nop Mcand: 0010 P: 0001 1000
2. Shr P Mcand: 0010 P: 0000 1100
1. 0=>nop Mcand: 0010 P: 0000 1100
2. Shr P Mcand: 0010 P: 0000 0110

## Slide 36: Observations: Multiply Ver. 2
2 steps per bit because multiplier and product registers combined
What about signed multiplication?
  The easiest solution is to make both positive and remember whether to complement product when done (leave out sign bit, run for 63 steps)
  Apply definition of 2’s complement
    sign-extend partial products and subtract at end
  Booth’s algorithm: use same HW and save cycles

## Slide 37: Faster Multiplier
Use multiple adders: cost/performance tradeoff
Can be pipelined: several multiplications in parallel
Fig. 3.7

## Slide 38: RISC-V Integer Multiplication
mul: multiply
  Gives lower 64 bits of the product in destination register
mulh: multiply high
  Gives upper 64 bits of the product in destination register, assuming signed  signed
mulhu: multiply high unsigned
  Gives upper 64 bits of the product in destination register, assuming unsigned  unsigned
mulhsu: multiply high signed/unsigned
  Gives upper 64 bits of the product in destination register, assuming signed  unsigned
Use mulh result to check for 64-bit overflow
To get 128-bit product:
mulh[[s]u] rdh, rs1, rs2
mul rdl, rs1,rs2

## Slide 39: Outline
Addition and subtraction (Sec. 3.2)
Multiplication (Sec. 3.3)
Division (Sec. 3.4)
Floating point (Sec. 3.5)
Parallelism and computer arithmetic: subword parallelism (Sec. 3.6)
Streaming SIMD extensions and advanced vector extensions in x86 (Sec. 3.7)
Subword parallelism and matrix multiply (Sec. 3.8)

## Slide 40: Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division approach
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor

## Slide 41: Divide Hardware for RISC-V (Version 1)
128-bit Divisor register (initialized with 64-bit divisor in left half), 128-bit ALU, 128-bit Remainder register (initialized with 128-bit dividend), 64-bit Quotient register
Fig. 3.8

## Slide 42: Divide Algorithm (Version 1)
No: < 65 repetitions
2b. Restore original value by adding Divisor to Remainder, put sum in Remainder, shift Quotient to left, set new rightmost bit to 0
Test Remainder
Remainder < 0
Remainder  0
1. Subtract Divisor register from Remainder
register, place result in Remainder register
2a. Shift Quotient to left, set new rightmost bit to 1
3. Shift Divisor register right 1 bit
Done
Yes: 65 repetitions
Start: Place Dividend in Remainder
65th
repetition?
Quot. Divisor Remainder
0000 00100000 00000111
11100111
00000111
0000 00010000 00000111
11110111
00000111
0000 00001000 00000111
11111111
00000111
0000 00000100 00000111
00000011
0001 00000011
0001 00000010 00000011
00000001
0011 00000001
0011 00000001 00000001
Fig. 3.9
Notes: Q: 0000 D: 0010 0000 R: 0000 0111  = 1110 0000
1: R = R Q: 0000 D: 0010 0000 R: 1110 0111
2b: +D, sl Q, 0 Q: 0000 D: 0010 0000 R: 0000 0111
3: Shr D Q: 0000 D: 0001 0000 R: 0000 0111  = 1111 0000
1: R = R Q: 0000 D: 0001 0000 R: 1111 0111
2b: +D, sl Q, 0 Q: 0000 D: 0001 0000 R: 0000 0111
3: Shr D Q: 0000 D: 0000 1000 R: 0000 0111  = 1111 1000
1: R = R Q: 0000 D: 0000 1000 R: 1111 1111
2b: +D, sl Q, 0 Q: 0000 D: 0000 1000 R: 0000 0111
3: Shr D Q: 0000 D: 0000 0100 R: 0000 0111  = 1111 1100
1: R = R Q: 0000 D: 0000 0100 R: 0000 0011
2a: sl Q, 1 Q: 0001 D: 0000 0100 R: 0000 0011
3: Shr D Q: 0000 D: 0000 0010 R: 0000 0011  = 1111 1110
1: R = R Q: 0000 D: 0000 0010 R: 0000 0001
2a: sl Q, 1 Q: 0011 D: 0000 0010 R: 0000 0001
3: Shr D Q: 0011 D: 0000 0001 R: 0000 0001
Recommend show 2 comp of divisor, show lines for subtract divisor and restore remainder

## Slide 43: Observations: Divide Version 1
Half of the bits in divisor register always 0  1/2 of 128-bit adder is wasted  1/2 of divisor is wasted
Instead of shifting divisor to right, shift remainder to left?
1st step cannot produce a 1 in quotient bit (otherwise quotient is too big for the register)  switch order to shift first and then subtract  save 1 iteration
Eliminate Quotient register by combining with Remainder register as shifted left

## Slide 44: Divide Hardware (Version 2)
(Quotient)
64-bit Divisor register, 64-bit ALU, 128-bit Remainder register (0-bit Quotient register)
Fig. 3.11

## Slide 45: Divide Algorithm (Version 2)
Test Remainder
No: < 64 repetitions
Step Remainder Divisor 0 0000 0111 0010
1.1 0000 1110
1.2 1110 1110
1.3b 0001 1100
2.2 1111 1100
2.3b 0011 1000 3.2 0001 1000
3.3a 0011 0001
4.2 0001 0001
4.3a 0010 0011
0001 0011
Remainder < 0
Remainder  0
2. Subtract Divisor from left half of Remainder, put result in left half of Remainder
1. Shift Remainder register left 1 bit
Done. Shift left half of Remainder right 1 bit
Yes: 64 repetitions
64th
repetition?
Start: Place Dividend in Remainder
3b. Restore original value by adding Divisor to left half of Remainder, put sum there, shift Remainder to left, set new rightmost bit to 0
3a. Shift Remainder to left, setting new rightmost bit to 1
Notes: D: 0010 R: 0000 0111
0: Shl R D: 0010 R: 0000 1110
1: R = R D: 0010 R: 1110 1110
2b: +D, sl R, 0 D: 0010 R: 0001 1100
1: R = R D: 0010 R: 1111 1100
2b: +D, sl R, 0 D: 0010 R: 0011 1000
1: R = R D: 0010 R: 0001 1000
2a: sl R, 1 D: 0010 R: 0011 0001
1: R = R D: 0010 R: 0001 0001
2a: sl R, 1 D: 0010 R: 0010 0011
Shr R(rh) D: 0010 R: 0001 0011

## Slide 46: Signed Divide
Remember signs, make positive, complement quotient and remainder if necessary
Alternative: Let Dividend and Remainder have same sign, negate Quotient if Divisor sign and Dividend sign disagree
  e.g., -7 2 = -3, remainder = -1
  -7- 2 = 3, remainder = -1
  Satisfy Dividend = Quotient x Divisor + Remainder
Possible for quotient to be too large:
  If divide 64-bit integer by 1, quotient is 64 bits

## Slide 47: Observation: Multiply and Divide
Same hardware as multiply: just need ALU to add or subtract, and 128-bit register to shift left or shift right
Product/
Remainder
(Multiplier/
Quotient)
Multiplicand/
Divisor
64-bit ALU
Write
Control
64 bits
128 bits
Shift Left
Shift Right
64-bit Multiplicand/Divisor register, 64-bit ALU, 128-bit Product/Remainder register (0-bit Multiplier/Quotient register)

## Slide 48: Faster Division
Can’t use parallel hardware as in multiplier
  Subtraction is conditional on sign of remainder
Faster dividers (e.g. SRT devision) generate multiple quotient bits per step
  Still require multiple steps

## Slide 49: RISC-V Integer Division
div/divu: signed/unsigned division
  Gives 64-bit signed/unsigned quotient in destination register
rem/remu: signed/unsigned remainder
  Gives 64-bit signed/unsigned remainder of the division
If both quotient and remainder are required:
  div[u] rdq, rs1, rs2
  rem[u] rdr, rs1, rs2
  Microarchitectures can fuse them into a single division
Overflow and division-by-zero don’t produce errors
  Just return defined results
  Faster for the common case of no error

## Slide 50: Outline
Addition and subtraction (Sec. 3.2)
Multiplication (Sec. 3.3)
Division (Sec. 3.4)
Floating point (Sec. 3.5)
Parallelism and computer arithmetic: subword parallelism (Sec. 3.6)
Streaming SIMD extensions and advanced vector extensions in x86 (Sec. 3.7)
Subword parallelism and matrix multiply (Sec. 3.8)

## Slide 51: Floating-Point Numbers: Motivation
What can be represented in N bits?
Unsigned 0 to 2n - 1
2’s Complement -2n-1 to 2n-1- 1
But, what about ...
  very large numbers? 9,349,398,989,787,762,244,859,087,678
  very small number? 0.0000000000000000000000045691
  rationals 2/3
  irrationals 2
  transcendentals e, 
How to represent them in just N bits?

## Slide 52: Floating Point Numbers
In math, we use scientific notation to representation very small and very large numbers, e.g.,
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary:
Types float and double in C/C++
Normalized (exactly one non-zero digit to the left of decimal point)
Non-normalized
1.0two x 2-1
radix (base)
“binary point”
Significand (Mantissa)
exponent
Floating point: binary point is not fixed (vs. fixed-point numbers such as integers)

## Slide 53: Intuitive Floating Point Representation
Normalized format: 1.xxxxxxxxxxtwo  2yyyytwo
Can use 32 bits to represent (single-precision):
S represents sign Exponent represents y’s (positive or negative) Significand represents 1.x’s
Represent numbers from 2.0 x 10-38 to 2.0 x 1038
0
31
S
Exponent
30
23
22
Significand
1 bit
8 bits
23 bits
0
1
-1
1.xxxxxxxx
Fixed binary point
Notes: Consider 1.1111111…11 x 2^15
1.1111111…10 x 2^15

## Slide 54: Intuitive Floating Point Representation
Can use 64 bits if more precision is needed (double precision)
Double precision (vs. single precision)
  Represent numbers almost as small as 2.0 x 10-308 to almost as large as 2.0 x 10308
  Main advantage is greater accuracy due to larger significand
0
31
S
Exponent
30
20
19
Significand
1 bit
11 bits
20 bits
Significand (cont’d)
32 bits
1.xxxxxxxx
Notes: Compare 1.11111…10 x 2^15 and 1.11111…10 11111…11 x 2^15

## Slide 55: Floating Point Standard
Defined by IEEE Std 754-1985
  For portability; more efficient use of bits
  S: sign bit (0  non-negative, 1  negative)
  Normalized significand: 1.0 ≤ |significand| < 2.0
    Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)  to pack more bits
    Significand is Fraction with the “1.” restored
  Note: 0 has no leading 1, so reserve exponent value 0 just for number 0
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits

## Slide 56: Floating Point Standard
0
1111 1111
000 0000 0000 0000 0000 0000
1/2
0
0000 0001
000 0000 0000 0000 0000 0000
2
Handling exponent:
  Need to represent positive and negative exponents
  Also want to compare FP numbers as if they were integers
  If use 2’s complement to represent? e.g., 1.0 x 2-1 versus 1.0 x2+1 (1/2 versus 2)
  If we use integer comparison for these two words, we will conclude that 1/2 > 2!!!

## Slide 57: Floating Point Standard
Handling exponent: (cont.)
  Instead, let notation 0000 0000 be the most negative, and 1111 1111 the most positive  biased notation, where bias is the number subtracted to get the real number
  IEEE 754 uses bias of 127 (0111 1111) for single precision: subtract 127 from Exponent field to get actual value for exponent
  1023 (011 1111 1111) is bias for double precision
1/2
0
0111 1110
000 0000 0000 0000 0000 0000
0
1000 0000
000 0000 0000 0000 0000 0000
2

## Slide 58: Floating Point Standard
Summary (single precision):
(-1)S x (1.Fraction) x 2(Exponent-127)
Double precision identical, except with exponent bias of 1023
0
31
S
Exponent
30
23
22
Fraction
1 bit
8 bits
23 bits

## Slide 59: Single Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  Exponent: 11111110  actual exponent = 254 – 127 = +127
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 60: Double Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 61: Floating Point Precision
Relative precision
  All fraction bits are significant
  Single precision: approximately 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double precision: approximately 2–52
    Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision

## Slide 62: Floating Point Example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single precision: 1011111101000…00
Double precision: 1011111111101000…00

## Slide 63: Floating Point Example
A more difficult case: representing 1/3?
  = 0.33333…10 = 0.0101010101… 2  20
  = 1.0101010101… 2  2-2
  Sign: 0
  Exponent = -2 + 127 = 12510=011111012
  Fraction = 0101010101…
  This 32-bit number is only an approximation of 1/3! If we use this number as 1/3 in subsequent computations, the error will propagate and magnify
0
0111 1101
0101 0101 0101 0101 0101 010

## Slide 64: Floating Point Example
What number is represented by the single-precision floating point?
11000000101000…00
  S = 1
  Fraction = 01000…002
  Exponent = 100000012 = 129
x = (–1)1 × (1 + 0.012) × 2(129 – 127) = (–1) × 1.25 × 22 = –5.0
Can it also represent the following number?
1
1000 0001
0100 0000 0000 0000 0000 000
01

## Slide 65: Special Numbers in IEEE 754 Standard
So far, we have not used the full range of 32/64 bits in defining floating point numbers
Consider single precision representation:
Exponent Fraction Object
0 0 ???
0 nonzero ???
1-254 anything +/- floating-point
255 0 ???
255 nonzero ???
+/- 0

## Slide 66: Denormalized Numbers
Represent denormalized numbers (denorms)
  Exponent: 000...0
  Fraction: non-zeroes  hidden bit is 0
  Allow a number to degrade in significance until it become 0 (gradual underflow)
  Smallest normalized number
    1.0000 0000 0000 0000 0000 000  2-126
  Smallest de-normalized number
    0.0000 0000 0000 0000 0000 001  2-126
0
0000 0000
0100 0000 0000 0000 0000 000
= 0.012  2-126

## Slide 67: Special Numbers in IEEE 754 Standard
So far, we have not used the full range of 32/64 bits in defining floating point numbers
Consider single precision representation:
Exponent Fraction Object
0 0 +/- 0
0 nonzero denorm
1-254 anything +/- floating-point
255 0 ???
255 nonzero ???
  Denormal with fraction = 000...0
Two representations of 0.0!

## Slide 68: Representation for +/- Infinity
In FP, divide by zero should produce +/- infinity, not overflow
Why?
  OK to do further computations with infinity, e.g., X/0 > Y may be a valid comparison
IEEE 754 represents +/- infinity
  Most positive exponent reserved for infinity
  Fraction is all zeroes
S
1111 1111
0000 0000 0000 0000 0000 000

## Slide 69: Special Numbers in IEEE 754 Standard
So far, we have not used the full range of 32/64 bits in defining floating point numbers
Consider single precision representation:
Exponent Fraction Object
0 0 +/- 0
0 nonzero denorm
1-254 anything +/- floating-point
255 0 +/- infinity
255 nonzero ???

## Slide 70: Representation for Not a Number
What do I get if I calculate sqrt(-4.0) or 0/0?
  If infinity is not an error, these should not be either
  They are called Not a Number (NaN)  Exponent = 255, Fraction nonzero
Why is this useful?
  Indicates illegal or undefined result
  Hope NaNs help with debugging
  They contaminate: op(NaN, X) = NaN
  OK if calculate but don’t use it

## Slide 71: Summary: IEEE 754 FP Standard
Fig. 3.13

## Slide 72: Floating Point Addition
Consider a 4-digit decimal example 9.999 × 101 + 1.610 × 10–1
1) Align decimal points
  Shift number with smaller exponent
  9.999 × 101 + 0.016 × 101
2) Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3) Normalize result and check for over/underflow
  1.0015 × 102
4) Round and renormalize if necessary
  1.002 × 102

## Slide 73: Floating Point Addition
Now consider a 4-digit binary example 1.0002 × 2–1 + –1.1102 × 2–2 (0.5 + –0.4375)
1) Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2) Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3) Normalize result and check for over/underflow
  1.0002 × 2–4, with no over/underflow
4) Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.0625

## Slide 74: FP Adder Hardware
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
FP adder usually takes several cycles
  Can be pipelined

## Slide 75: FP Adder
Step 1
Step 2
Step 3
Step 4
Fig. 3.15

## Slide 76: Floating Point Multiplication
Consider a 4-digit decimal example 1.110 × 1010 × 9.200 × 10–5
1) Add exponents
  For biased exponents, subtract bias from sum
  New exponent = 10 + –5 = 5
2) Multiply significands
  1.110 × 9.200 = 10.212  10.212 × 105
3) Normalize result and check for over/underflow
  1.0212 × 106
4) Round and renormalize if necessary
  1.021 × 106
5) Determine sign of result from signs of operands
  +1.021 × 106

## Slide 77: Floating Point Multiplication
Now consider a 4-digit binary example 1.0002 × 2–1 × –1.1102 × 2–2 (0.5 × –0.4375)
1) Add exponents
  Unbiased: –1 + –2 = –3
  Biased: (–1 + 127) + (–2 + 127) = –3 + 254 – 127 = –3 + 127
2) Multiply significands
  1.0002 × 1.1102 = 1.1102  1.1102 × 2–3
3) Normalize result and check for over/underflow
  1.1102 × 2–3 (no change) with no over/underflow
4) Round and renormalize if necessary
  1.1102 × 2–3 (no change)
5) Determine sign: +ve × –ve  –ve
  –1.1102 × 2–3 = –0.21875

## Slide 78: FP Arithmetic Hardware
FP multiplier is of similar complexity to FP adder
  But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root
  FP  integer conversion
Operations usually takes several cycles
  Can be pipelined

## Slide 79: FP Instructions in RISC-V
Separate FP registers: f0, …, f31
  double-precision
  single-precision values stored in the lower 32 bits
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
FP load and store instructions
  Single precision load/store: flw, fsw
  Double precision load/store: fld, fsd

## Slide 80: FP Instructions in RISC-V
Single-precision arithmetic
  fadd.s, fsub.s, fmul.s, fdiv.s, fsqrt.s
    e.g., fadds.s f2, f4, f6
Double-precision arithmetic
  fadd.d, fsub.d, fmul.d, fdiv.d, fsqrt.d
    e.g., fadd.d f2, f4, f6
Single- and double-precision comparison
  feq.s, flt.s, fle.s
  feq.d, flt.d, fle.d
  Result is 0 or 1 in integer destination register
feq.d x5,f0,f1

## Slide 81: FP Example: °F to °C
C code:
float f2c(float fahr) { return ((5.0/9.0)*(fahr - 32.0)); }
  fahr in f10, result in f10, literals in global memory space
Compiled RISC-V code:
f2c: flw f0,const5(x3) // f0 = 5.0f
flw f1,const9(x3) // f1 = 9.0f
fdiv.s f0,f0,f1 // f0 = 5.0f/9.0f
flw f1,const32(x3) // f1 = 32.0f
fsub.s f10,f10,f1 // f10 = fahr–32.0
fmul.s f10,f0,f10 // f10 = () * ()
jalr x0,0(x1) // return

## Slide 82: FP Example: Array Multiplication
C = C + A × B
  All 32 × 32 matrices, 64-bit double-precision elements
C code:
void mm (double c[][], double a[][], double b[][]) { size_t i, j, k; for (i = 0; i < 32; i = i + 1) for (j = 0; j < 32; j = j + 1) for (k = 0; k < 32; k = k + 1) c[i][j] = c[i][j] + a[i][k] * b[k][j]; }
  Addresses of c, a, b in x10, x11, x12, and i, j, k in x5, x6, x7

## Slide 83: FP Example: Array Multiplication
RISC-V code:
mm:...
li x28,32 // x28 = 32 (row size/loop end)
li x5,0 // i = 0; initialize 1st for loop
L1: li x6,0 // j = 0; initialize 2nd for loop
L2: li x7,0 // k = 0; initialize 3rd for loop
slli x30,x5,5 // x30 = i * 2**5 (size of row of c)
add x30,x30,x6 // x30 = i * size(row) + j
slli x30,x30,3 // x30 = byte offset of [i][j]
add x30,x10,x30 // x30 = byte address of c[i][j]
fld f0,0(x30) // f0 = c[i][j]
L3: slli x29,x7,5 // x29 = k * 2**5 (size of row of b)
add x29,x29,x6 // x29 = k * size(row) + j
slli x29,x29,3 // x29 = byte offset of [k][j]
add x29,x12,x29 // x29 = byte address of b[k][j]
fld f1,0(x29) // f1 = b[k][j]

## Slide 84: FP Example: Array Multiplication
RISC-V code:
li x28,32 // x28 = 32 (row size/loop end)
li x5,0 // i = 0; initialize 1st for loop
L1: li x6,0 // j = 0; initialize 2nd for loop
L2: li x7,0 // k = 0; initialize 3rd for loop
slli x30,x5,5 // x30 = i * 2^5 (size of row of c)
add x30,x30,x6 // x30 = i * size(row) + j
slli x30,x30,3 // x30 = byte offset of [i][j]
add x30,x10,x30 // x30 = byte address of c[i][j]
fld f0,0(x30) // f0 = c[i][j]
L3: slli x29,x7,5 // x29 = k * 2^5 (size of row of b)
add x29,x29,x6 // x29 = k * size(row) + j
slli x29,x29,3 // x29 = byte offset of [k][j]
add x29,x12,x29 // x29 = byte address of b[k][j]
fld f1,0(x29) // f1 = b[k][j]

## Slide 85: FP Example: Array Multiplication
slli x29,x5,5 // x29 = i * 2^5 (size of row of a)
add x29,x29,x7 // x29 = i * size(row) + k
slli x29,x29,3 // x29 = byte offset of [i][k]
add x29,x11,x29 // x29 = byte address of a[i][k]
fld f2,0(x29) // f2 = a[i][k]
fmul.d f1, f2, f1 // f1 = a[i][k] * b[k][j]
fadd.d f0, f0, f1 // f0 = c[i][j] + a[i][k] * b[k][j]
addi x7,x7,1 // k = k + 1
bltu x7,x28,L3 // if (k < 32) go to L3
fsd f0,0(x30) // c[i][j] = f0
addi x6,x6,1 // j = j + 1
bltu x6,x28,L2 // if (j < 32) go to L2
addi x5,x5,1 // i = i + 1
bltu x5,x28,L1 // if (i < 32) go to L1

## Slide 86: Accurate Arithmetic
Integer arithmetic is accurate
  Because integers can represent exactly every number between the smallest and largest number
FP arithmetic is approximate
  Because FP numbers are just approximations for the actual number they want to represent
  The approximation errors widen as FP numbers are operated upon to generate new FP numbers
  Need to be careful in rounding intermediate results
IEEE Std 754 specifies additional rounding control
  Use extra bits during HW calculation to preserve precision (guard, round, sticky) and allow choice of rounding modes
Notes: IEEE Std 754 specifies additional rounding control
  Extra bits of precision (guard, round, sticky)
  Choice of rounding modes
  Allows programmer to fine-tune numerical behavior of a computation
Not all FP units implement all options
  Most programming languages and FP libraries just use defaults
Trade-off between hardware complexity, performance, and market requirements

## Slide 87: Associativity of FP Operations
Is FP add/subtract associative?
FP add/subtract are not associative!
  Why? FP result approximates real result!
  Ex: 1.5 x 1038 is so much larger than 1.0 that 1.5 x 1038 + 1.0 in floating point representation is still 1.5 x 1038
 |  | (X + Y ) + Z | X + (Y + Z)
X | -1.50 x 1038 |  | -1.50 x 1038
Y | 1.50 x 1038 | 0.0 | 
Z | 1.0 | 1.0 | 1.50 x 1038
 |  | 1.0 | 0.0

## Slide 88: Outline
Addition and subtraction (Sec. 3.2)
Multiplication (Sec. 3.3)
Division (Sec. 3.4)
Floating point (Sec. 3.5)
Parallelism and computer arithmetic: subword parallelism (Sec. 3.6)
Streaming SIMD extensions and advanced vector extensions in x86 (Sec. 3.7)
Subword parallelism and matrix multiply (Sec. 3.8)

## Slide 89: Arithmetic for Multimedia
Graphics and media processing often perform same operations on vectors of 8-bit and 16-bit data
  These data are often packed into words
How to operate on these words of short data?
  Since we have already had 64-bit adder, can we leverage it?
  Partition the carry chain of the 64-bit adder so that the adder can perform 8 8-bit or 4 16-bit vector add/sub
  This is called subword parallelism
Saturating operations
  On overflow, result is the largest representable value, e.g., clipping in audio, saturation in video

## Slide 90: Subword Parallelism
An 8-bit ripple-carry adder:
Turned into 2 4-bit ripple-carry adder:
X
http://ece-research.unm.edu/pollard/classes/338/lademo/LookAheadDemo.htm
0

## Slide 91: Fallacies and Pitfalls
Left shift by i places  multiplies an integer by 2i
Right shift by i places divides by 2i?
  Only for unsigned integers
For signed integers
  Arithmetic right shift: replicate the sign bit
  e.g., –5 / 4 111110112 >> 2 = 111111102 = –2
    Rounds toward –∞
  If we only do logic shift right, 111110112 >> 2 = 001111102 = +62

## Slide 92: Summary
MIPS arithmetic: successive refinement to final design
  64-bit adder and logic unit
  64-bit multiplier and divisor
FP numbers approximate values that we want to use
  IEEE 754 Standard is most widely accepted representation
  New RISC-V registers (f0~f31) and instructions:
    Single-precision (32 bits): fadd.s, fsub.s, fmul.s, fdiv.s, fsqrt.s , feq.s, flt.s, fle.s
    Double-precision (64 bits): fadd.d, fsub.d, fmul.d, fdiv.d, fsqrt.d, feq.d, flt.d, fle.d

## Slide 93: Concluding Remarks
Bits have no inherent meaning
  Interpretation depends on the instructions applied
Computer representations of numbers
  Finite range and precision
  Need to account for this in programs
ISAs support arithmetic
  Signed and unsigned integers
  Floating-point approximation to reals
Bounded range and precision
  Operations can overflow and underflow