## Slide 1: CS4100: Computer Architecture The Processor (I)
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Outline
Problem statement and logic review (Sec. 4.1, 4.2)
Building a simple RISC-V processor with datapath and control (Sec. 4.3, 4.4)
Building a pipelined RISC-V processor with datapath and control (Sec. 4.5, 4.6)
Dealing hazards in pipelined processor: data and control hazards (Sec. 4.7, 4.8)
Handling exceptions (Sec. 4.9)
More advanced topics: parallelism via instructions, ARM Cortex-A53 and Intel Core i7 Pipelines, instruction-level parallelism (Sec. 4.10, 4.11, 4.12)

## Slide 3: Problem Statement: Design a RISC-V CPU
We have already seen the design of a simple 64-bit ALU that performs and/or/add/sub/set-less-than/nor operations
We are now ready to study the design of the whole processor: datapath + control
ALUop | Function
0000 | and
0001 | or
0010 | add
0110 | sub
0111 | set-less-than
1100 | nor
Register
ALU
CPU
ALUop
V
Z
PC
Controller
clock

## Slide 4: Two Designs of a Subset RISC-V CPU
Note that the design of a processor will affect its performance in terms of CPI and cycle time
  While instruction count is determined by ISA and compiler
We will examine two RISC-V implementations
  A simplified version: one (long) cycle per instruction
  A more realistic pipelined version: up to 5 cycles for an instruction, but potentially can complete one instruction per cycle (CPI = 1) using a shorter cycle time
Simple subset, shows most aspects
  Memory reference: ld, sd
  Arithmetic/logical: add, sub, and, or
  Control transfer: beq
Match our 64-bit ALU

## Slide 5: The RISC-V Subset
R-Type:
  add rd,rs1,rs2
  sub rd,rs1,rs2
  and rd,rs1,rs2
  or rd,rs1,rs2
I-type:
  ld rd,imm12(rs1)
S-type:
  sd rs2,imm12(rs1)
SB-type:
  beq rs,rt,imm12
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits
im[11:5]
rs2
rs1
im[4:0]
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
rs2
rs1
funct3
opcode
im [4:1]
imm[12]
imm[11]
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
im[10:5]
Notes: The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register. (Note that dest is the Rt field!)
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to from the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specified the registers we need to compare.
If these two registers are equal, we will branch to a location offset by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 6: Steps in Executing an Instruction
Step 1: fetch next instruction pointed to by PC from (instruction) memory
  Also do PC + 4
Z
V
Register
Memory
0008…10
Controller
ALU
clock
Control signals
Datapath
Control
PC
0008…10
015A04B3
015A04B3
0008…14

## Slide 7: Steps in Executing an Instruction
Step 2: decode and read register operands (rs2, rs1)
  Disregarding the type of the instruction
Z
V
Register
Memory
0008…10
Controller
ALU
clock
Control signals
Datapath
Control
PC
0008…10
015A04B3
015A04B3
20
21
0000000
10101
10100
01001
000
0110011
0008…14

## Slide 8: Steps in Executing an Instruction
Step 3: execute according to instruction type
  Arithmetic/logical: add, sub, and, or
    Controller sets ALU to perform the operation
Z
V
Register
Memory
0008…10
Controller
clock
Control signals
Datapath
Control
PC
0008…10
015A04B3
015A04B3
20
21
+
ALU
0008…14

## Slide 9: Steps in Executing an Instruction
Step 3 (cont.)
  Memory reference: ld, sd
    Calculate memory address = rs1 + 12-bit immediate
Z
V
Register
Memory
0008…10
Controller
clock
Control signals
Datapath
Control
PC
0008…10
078A3683
078A3683
20
21
+
X
ALU
0008…14

## Slide 10: Steps in Executing an Instruction
Step 3 (cont.)
  Conditional branch: beq
    Calculate target address = PC + {immediate | 0}
Z
V
Register
Memory
0008…10
Controller
clock
Control signals
Datapath
Control
PC
0008…10
FF5A06E7
FF5A06E7
20
21
+
X
X
ALU
0008…14

## Slide 11: Steps in Executing an Instruction
Step 4: write register back and memory access
  Arithmetic/logical: add, sub, and, or
    Write ALU result back to register rd, write (PC + 4) into PC
    Go to Step 1
Z
V
Register
Memory
0008…10
Controller
clock
Control signals
Datapath
Control
PC
0008…10
015A04B3
015A04B3
9
+
ALU
0008…14

## Slide 12: Steps in Executing an Instruction
Step 4 (cont.)
  Memory reference: ld
    Load memory from target address
Z
V
Register
Memory
0008…10
Controller
clock
Control signals
Datapath
Control
PC
0008…10
078A3683
078A3683
+
ALU
0008…14

## Slide 13: Steps in Executing an Instruction
Step 4 (cont.)
  Memory reference: sd
    Store rs2 to memory, write (PC + 4) into PC
    Go to Step 1
Z
V
Register
Memory
0008…10
Controller
clock
Control signals
Datapath
Control
PC
0008…10
075A3C23
075A3C23
21
+
ALU
0008…14

## Slide 14: Steps in Executing an Instruction
Step 4 (cont.)
  Conditional branch: beq
    Load PC and go to Step 1
Z
V
Register
Memory
0008…10
Controller
clock
Control signals
Datapath
Control
PC
0008…10
FF5A06E7
FF5A06E7
+
ALU
0008…94
0008…14

## Slide 15: Steps in Executing an Instruction
Step 5: write register back
  Memory reference: ld
    Load rd from memory, write (PC + 4) into PC
    Go to Step 1
Z
V
Register
Memory
00080010
Controller
clock
Control signals
Datapath
Control
PC
00080010
078A3683
078A3683
9
+
ALU
0008…14

## Slide 16: Logic Design Basics
Combinational element
  Operate on data
  Output is a function of input
  AND gate: Y = A & B Adder: Y = A + B
  Multiplexer: Y = S ? I1 : I0 ALU: Y = F(A, B)
A
B
Y
I0
I1
Y
Mux
S
A
B
Y
+
A
B
Y
ALU
F

## Slide 17: Logic Design Basics
State (sequential) elements
  Store information
Register: store data in a circuit
  Use clock signal to determine when to update stored value
  Edge-triggered: update when Clk changes from 0 to 1
    Avoid race condition
D
Clk
Q
Clk
D
Q

## Slide 18: Logic Design Basics
Register with write control
  Only updates on clock edge when write control input is 1
  Used when stored value is required later
D
Clk
Q
Write
Write
D
Q
Clk

## Slide 19: Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges if edge-triggered
  Input from state elements, output to state element
  Longest delay determines clock period
Fig. 4.3
Fig. 4.4
No race if edge-triggered
Notes: Fig. 4.3: In a synchronous digital system, the clock determines when elements with state will write values into internal storage. Any inputs to a state element must reach a stable value (that is, have reached a value from which they will not change until after the clock edge) before the active clock edge causes the state to be updated.
Fig. 4.4: An edge-triggered methodology allows a state element to be read and written in the same clock cycle without creating a race that could lead to indeterminate data values. Of course, the clock cycle still must be long enough so that the input values are stable when the active clock edge occurs. Feedback cannot occur within one clock cycle because of the edge-triggered update of the state element.

## Slide 20: Notes on Instruction Execution
The processor is a big sequential circuit
For simplified implementation of the RISC-V processor (one cycle/instruction), all steps for executing an instruction are performed within one clock cycle
  No matter whether the instruction takes 3, 4, or 5 steps
  Register/memory behaves like a combinational circuit if it is read
Write register/memory occurs only at the last step
  Recall edge-triggered update of state elements

## Slide 21: Outline
Problem statement and logic review (Sec. 4.1, 4.2)
Building a simple RISC-V processor with datapath and control (Sec. 4.3, 4.4)
Building a pipelined RISC-V processor with datapath and control (Sec. 4.5, 4.6)
Dealing hazards in pipelined processor: data and control hazards (Sec. 4.7, 4.8)
Handling exceptions (Sec. 4.9)
More advanced topics: parallelism via instructions, ARM Cortex-A53 and Intel Core i7 Pipelines, instruction-level parallelism (Sec. 4.10, 4.11, 4.12)

## Slide 22: Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a RISC-V datapath incrementally for the subset of instructions
  Memory reference: ld, sd
  Arithmetic/logical: add, sub, and, or
  Control transfer: beq

## Slide 23: Datapath for Instruction Fetch
Recall Step 1 in instruction execution:
  Fetch next instruction pointed to by PC from instruction memory and perform PC + 4
64-bit register
Increment by 4 for next instruction
Fig. 4.6

## Slide 24: Components for R-Type Instructions
Read two register operands from register file
Perform arithmetic/logical operation on ALU
Write register result back to register file
Fig. 4.7
0
6
12
15
20
25
31
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
24
19
14
11
7
rs1
rs2
rd

## Slide 25: Components for Load/Store Instructions
Read register operands
Calculate address using 12-bit offset
  Use ALU, but sign-extend offset
Load: Read data memory and update register
Store: Write register value to data memory
Fig. 4.8
32-bit instruction
64-bit target address

## Slide 26: Components for Branch Instructions
Read register operands
Compare operands
  Use ALU, subtract register operands and check Zero output
Calculate target address
  Target address = PC + {immediate|0}
  Sign-extend displacement
  Shift left 1 bit (halfword displacement)
  Add to PC value
rs2
rs1
funct3
opcode
im [4:1]
imm[12]
imm[11]
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
im[10:5]

## Slide 27: Components for Branch Instructions
Just re-routes wires
Sign-bit wire replicated
for sign-extending imm
Compare operands
Fig. 4.9

## Slide 28: Composing the Elements into CPU
First-cut data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 29: R-Type/Load/Store Datapath
Fig. 4.10
Register
Memory
PC
ALU

## Slide 30: Full Datapath
Fig. 4.11
CPI = 1
State elements:
PC, registers, memory (for sd, otherwise act as combinational elements)
sd
R-type, ld
2 memories
ALUctr
Notes: First-cut datapath does one instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories

## Slide 31: Data Flow for add During the Cycle
100..000

Fig. 4.11
Ckt
ALUctr

## Slide 32: Controller Design
ALUSrc
MemRd
MemtoReg
MemWr
Z
Instruction<31:0>
<15:19>
<12:14>
<7:11>
<0:6>
op
rd
func3
rs1
PCsrc
Addr
Instr.
Memory
Datapath
func7
<20:24>
rs2
RegWr
<25:31>
ALUctr
4
Controller
Main control
ALUOp
2
ALU control
4

## Slide 33: Datapath with Control
Fig. 4.17
PCsrc
OPcode
func3/func7

## Slide 34: Let’s Work on ALU Control
Recall ALU design in Chapter 3
ALU in RISC-V subset:
  Load/Store: Function = add  ALUOp = 00
  Branch: Function = subtract  ALUOp = 01
  R-type: Function depends on opcode/func  ALUOp = 10
ALUctr | Function
0000 | and
0001 | or
0010 | add
0110 | sub
0111 | set-less-than
1100 | nor
ALUOp
2
ALU control
4
ALUctr
func3/func7

## Slide 35: Design of ALU Control
Use the 2-bit ALUOp from the main control, which is derived from op code
Fig. 4.12
opcode | ALUOp | Operation | func7 | func3 | ALU function | ALUctr
ld | 00 | load double | XXXXXXX | XXX | add | 0010
sd | 00 | store double | XXXXXXX | XXX | add | 0010
beq | 01 | branch on eq. | XXXXXXX | XXX | subtract | 0110
R-type | 10 | add | 0000000 | 000 | add | 0010
 |  | subtract | 0100000 | 000 | subtract | 0110
 |  | AND | 0000000 | 111 | AND | 0000
 |  | OR | 0000000 | 110 | OR | 0001

## Slide 36: Truth Table for ALUctr
Fig. 4.13
The logic gate design of ALU control can then be derived easily
Fig. C.2.3
ALUctr
Logic design for MIPS

## Slide 37: Now, Let’s Work on Main Control
Consider R-type instruction
Fig. 4.19

## Slide 38: Control Signals for R-Type Instructions
Fig. 4.22

## Slide 39: Control for Load Instruction
Fig. 4.20

## Slide 40: Control Signals for Load Instructions
Fig. 4.22

## Slide 41: Control for Branch Instruction
Fig. 4.21

## Slide 42: Control Signals for Load Instructions
Fig. 4.22

## Slide 43: Design of Main Control
Fig. C.2.5
Unfortunately, we don’t have the main control logic circuit for RISC-V. Here is the design for MIPS processor.

## Slide 44: Performance Issues
CPI = 1 with a long cycle time
Longest delay determines clock period
  Critical path: ld instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We will improve performance by pipelining